## Slide 1: Construction Equipment Visibility

## Slide 2: How do back over incidents occur?
Drivers may not be able to see a worker in their blind spot.
Workers may not hear backup alarms because of other worksite noises or because the alarms are not functioning.
A spotter assisting one truck may not see another truck behind them.
Workers riding on vehicles may fall off and get backed over.
Drivers may assume that the area is clear and not look in the direction of travel.

## Slide 3: Construction Equipment Visibility
Sometimes, it is unclear why a worker was in the path of a backing vehicle. A combination of factors can also lead to back over incidents.
OSHA states that dump trucks, and pickups, are responsible for the majority of backing incidents in the past ten years on the job.
NCDOT recommends that specific procedures and controls be in place at roadway construction worksites to help prevent injuries and deaths from backing construction vehicles and equipment.

## Slide 4: Why it's important
According to a Bureau of Labor Statistics review of the 962 fatal workplace injuries throughout the United States over past several years at road construction sites, 443 were due to a worker being struck by a vehicle or mobile equipment.
Workers were fatally struck 143 times by a vehicle or mobile equipment that was backing up. In 84 of these cases, the worker was fatally struck by a dump truck that was backing up.

## Slide 5: Why it's important: Equipment Operation and Servicing
Ensure that construction vehicles and equipment operating onsite are always maintained in safe operating condition.
A scheduled maintenance program for all roadway construction vehicles and equipment.
Safety features (reverse alarm, video cameras) installed in accordance with manufacturer’s specifications, that operate as intended, and function properly.
Inspection of all vehicles, equipment, and safety devices (brakes, lights, horns, and reverse alarms) at the beginning of each work shift. Defective vehicles, equipment, and safety devices should be immediately reported and removed from service until repairs are made.
Installed collision avoidance or proximity warning systems are functioning properly.

## Slide 6: Why it's important: Vehicle and Equipment Operators
Inspect your vehicle, equipment, and safety devices (reverse alarm, mirrors, and windows) at the beginning of each shift and report any deficiencies to your supervisor; remove any defective equipment from service until repairs are made.
Ensure mirrors and windows are functioning, in good condition, clean and properly adjusted.
Be aware of equipment and vehicle blind areas and watch for workers.
Use and maintain contact (visually, verbally, or by hand signals) with a spotter when backing any vehicle or equipment.
If contact with the spotter is lost, STOP immediately.

## Slide 7: Why it's important: Backing Safety Solutions Spotter
Spotters are a proven method of protecting employees on foot behind vehicles with an obstructed view, but spotters themselves can be at risk for injury or even death. We can implement the following actions to help keep spotters safe:
Ensure that spotters and drivers agree on hand signals before backing up.
Instruct spotters to always maintain visual contact with the driver while the vehicle is backing.
Instruct drivers to stop backing immediately if they lose sight of the spotter.
Do Not give spotters additional duties while they are acting as spotters.
Instruct spotters not to use personal mobile phones, personal headphones, or other items which could pose a distraction during spotting activities.
Provide spotters with high-visibility clothing, especially during night operations.

## Slide 8: Why it's important Workers on Foot
Always wear high visibility apparel that is appropriate for your job task and work environment.
Be aware of equipment and vehicle blind areas and avoid being near these areas.
Confirm communications signals with an operator and do not approach until the operator gives acknowledgment.
Be aware of equipment travel paths and avoid standing or walking in these areas.
LISTEN for reverse signal alarms in the area.
Do not rely solely on one safety practice, always be aware of your surroundings and ensure that workers are aware of you.

## Slide 9: Backing events require extreme caution
Backing accidents are the most frequent type of accidents in all of construction
If you must back up, GET OUT AND LOOK
Check for proper clearance on all six sides: up, down, left, right, front, and rear
Continue to GET OUT AND LOOK multiple times
Don’t just think you’re clear, KNOW you’re clear: GET OUT AND LOOK
Using a spotter to assist is always recommended
Even with spotter, it is the driver’s responsibility to not strike anything
GET OUT AND LOOK, even if a spotter is flagging you back

## Slide 10: While You Are Backing
Back from the driver’s side
  Minimize the distance you need to back. The less ground you cover in reverse; the less chances you will have made-up a fixed object.
Have patience & don’t rush
  No one ever made-up time by backing quickly. Take a deep breath and commit yourself to perfect backing with no compromises.
  Slow movement helps you maintain full control of your vehicle and to correctly judge distances.
Check all sides as you back
  Remember that there are 6 sides to your vehicle (back, front, both sides, above and below).
  Keep your eyes moving to ensure conditions have not changed.
Use always keep your spotter in sight your resources and guides
  Use a spotter if someone is available. Be sure to keep your spotter in sight at all times.
  Make sure your mirrors are clean and in good positions to maximize the view around your vehicle – Know your blind spots!
  Roll down your window and listen to the environment around you.