## Slide 1: Integrating Generative AI with Traditional Urban Economics for Long-Range LUTI Modeling
2025 Fall NCMUG Meeting November 20, 2025
Colby Brown, CEO, Manhan

## Slide 2: CONTEXT: GROWTH IN GREATER ASHEVILLE

## Slide 3: Alternative Future Scenarios Developed by FBRMPO
Baseline (market-driven)
Projections consistent with State Demographer
Build-out capacity based upon current LU trends
Include known development projects
Accelerated (higher growth)
Doubled household growth rate (starting in 2030)
Reduce external-internal trip volumes
Consolidated (higher density)
Prefer areas that are walkable and/or served by transit
Increase multi-family housing share
Conserve green space
Dispersed (lower density)
Lower maximum density constraints
Open up land for development

## Slide 4: Land Use / Transport Interaction (LUTI)
Base year run (calibrated to traffic counts)
2020 Travel Model
Interim year run; accessibility metrics
2030 Travel Model
Interim year run; accessibility metrics
2040 Travel Model
Final horizon year run; VMT reporting
2050 Travel Model
2040 Land Use
First feedback iteration; includes 2035 timestep
2030 Land Use
Includes known projects and Helene impacts
2050 Land Use
Second feedback iteration; includes 2045

## Slide 5: Land Use Forecasting System
Sensitive to:
Zoning codes
Generalized land use classification
Transit service
Sewer and wastewater
Steep slopes & elevation
Protected areas
Highway access
Market forces
Component | What it does | Data source
Land Use Change | Simulate realistic land use changes using neural network | FBRMPO’s existing land use (ELUSE) parcel data
Build-out analysis | Reflect availability of land for development (by type) | ELUSE and InfoUSA employment data
Flooding impact | Estimates impact of catastrophic flooding | North Carolina FINMAN; anonymized ICEYE data
Bidding model | Represents competition in the housing market | U.S. Census American Community Survey
Allocation model | Simulate real estate development location choices | 2014-2019 Census ACS; travel model; GIS data
Travel model | Represent congestion on highways & local roads | Maintained by NCDOT

## Slide 7: Existing Land Use and Build-out Capacity
 | Max Density (jobs per acre) | 
Type | Other Scenarios | Dispersed Scenario
Industrial | 16.4 | 5.2
Commercial | 41.6 | 13.1
Lodging | 11.1 | 4.0
Office | 57.9 | 19.2
Mixed-Use | 30.8 | 6.1
Institutional | 14 | 3.1
Special | 25 | 1.1
Notes: FBRMPO maintains a parcel layer with existing land use, updated every 5 years since 2000
  Residential LU types are defined using maximum density values
  Non-residential max density estimated using InfoUSA data
  Can be used to calculate build-out capacity by land use type
However, land uses change!

## Slide 8: Future Land Use Prediction (1)
Land uses change!
LLMs are good at predicting “next token” in sequence
Experiment:
  Code land use change history as text, with context
  Fine-tune an LLM on this “corpus”

## Slide 9: Future Land Use Prediction (2)
Selected model: StarCoder (v1)
  Primarily a code model—unlikely that natural language use of words in training data will bias results
  Base training process excluded copyrighted works from dataset
  Smaller versions available to lighten the computation load
  Supports relatively long context
  Compatible with GGUF, Ollama
Train using Transformers library

## Slide 10: Future Land Use Prediction (3)
Land Use Change Language Model (LUC-LM) results:
  Over 92% accuracy for non-residential land uses
  Over 80% accuracy for residential
  Outperformed previous attempt using a conventional neural net
However, model is slow, even on GPU and with optimizations
Solution: screening model to determine likelihood of change

## Slide 11
2020-2025

## Slide 12
2025-2030

## Slide 13
2030-2035

## Slide 14
2035-2040

## Slide 15
2040-2045

## Slide 16
2045-2050

## Slide 17
TAZ
Block
Parcel
LUC-LM
ELUSE
ELUSE
ALLOCATION
ACCESS
MPI
BUILD-OUT
CAPACITY
BID-AUCTION
SE DATA
MPI
UNITS
Prior Time-Step
Current Time-Step

## Slide 18: Allocation Model (OLAF)
Constrained location choice with Monte Carlo simulation
Incorporate known projects and estimated build-out capacity
Allow allocation of declines as well as growth (job loss, housing churn)
Suitability functions estimated from observed dynamics; use MPI
Land Suitability
(accessibility, infrastructure, buffers)
Constraints (natural & human)

## Slide 19: Residential Bid Model
Choice of occupant
  Maximize bid / utility
Household/job characteristics
  Size (persons per HH/firm)
  Income (per HH/employee)
Area characteristics
  Transportation accessibility
  Household and job density
  Other area characteristics
Housing unit type

## Slide 20: CONCLUSIONS
Applications of generative AI in urban planning and travel forecasting may not look like they do in other fields
Language models can be helpful for more than question-answer chatbots
It’s possible to develop and apply AI without infringing basic copyright or data dignity protections.
Useful AI applications can complement without replacing existing workflows
It’s easier to work at the spatial and temporal resolution that makes sense for the policy or data source at hand, rather than doing everything at the same level.

## Slide 21
Questions
And
Comments

## Slide 22
MANHAN
manhan.co
cbrown@manhan.co