## Slide 1: Model Spotlight: Metrolina Regional Travel Demand Model, MRM25
NC Model Users Group, Fall 2025
Martin Kinnamon, PE
Regional Modeling, Analysis and Coordination Section Manager, CDOT

## Slide 2
MRM Model Team Staff
Marlee Henninge
TP III
Martin Kinnamon
Section Manager
Dewan Parvez
Travel Demand Modeler
Torrey Williams
Senior Modeler
Alex Riemondy
Senior Modeler

## Slide 3: Metrolina Regional Model
13 Counties
  New! Anson
2 States
4 MPOs
2 RPOs
Greater Hickory MPO
Gaston – Cleveland – Lincoln MPO
Rock Hill – Fort Mill
Area Transportation Study
CRTPO
Cabarrus Rowan MPO
Rocky River RPO

## Slide 4: MRM Region
5,600 square miles
3,805 TAZs
2022:
  Approx. 2.9M People in 1.2M Households
  Approx. 1.7M jobs
2055:
  Approx. 4.7M People in 1.9M Households
  Approx. 2.5M jobs
Notes: 60% pop growth; current numbers of 157 people/day into region; Meck just under 40% of that

## Slide 5: Fast Growing Region: Employment Announcements in last few weeks:

## Slide 6: Input Updates in MRM25
  Household Travel Survey
    Conducted Fall 2023
    5,200+ households
  Transit On-Board Survey
    Conducted Fall 2022
  SE Data (household, employment, student enrollment)
    2022 base year data (provided by MPOs)
    County- and district-level totals updated Winter 2024
      Independent demographer/economist (Fouth Economy)
    Allocation to TAZs using CommunityViz (Coordinate Our Future, etc)
  Roadway and Transit Networks
    Webmap process
    Added Anson County

## Slide 7: MRM25 Updates -- Model components
  In-house:
    Commercial Vehicle model update
    Coding updates
  Consultant Led (Caliper):
    Update of previous tour models
    Added tour-based Mode Choice Model
    Moved intermediate stops after mode choice
    Coding updates

## Slide 8: MRM25 Updates -- New Flowchart User Interface TransCAD 10

## Slide 9: MRM25 Updates -- GitHub Tracking, Documentation, and Distribution

## Slide 10: Simplified Tour-Based Model
Early 2000s
  First Metrolina Regional Model (MRM) developed
2014
  Began work on tour-based model
  Used 2012 HHTS and External Survey Data
2017 – 2019
  Ran trip/tour-based model concurrently
  Trip model was still the official version (MRM18v1.0)
April 2019
  MRM19v1.0 endorsed as the first instance of the tour-based model for the region
May 2022
  Second instance released (MRM22v1.0)
January 2025
  MRM25v1.0used for RFATS’ 2055 MTP

## Slide 11: Trip vs Simplified Tour
Trip Generation
Trip Distribution
Mode Choice
Trip Assignment
Peak / Off-peak
AM / PM / Midday / Night
Feedback congested speeds
Tour Frequency
Tour Destination
Intermediate Stops
Trip Assignment
AM / PM / Midday / Night
Feedback congested speeds
Mode Choice
Highway & Transit Skims
Highway & Transit Skims
Feedback Skims
Feedback Skims

## Slide 12: Key Benefit: Modeling Households
Avoid aggregation bias
  using average data masks important differences
  more accurate to model individual behavior
Improved reporting
  more detailed cross-tabs of travel behavior
  better understanding of how system changes affect certain individuals
  helpful for Environmental Justice analyses

## Slide 13: Tour Frequency
Logit equations instead of trip rates
Discrete choices for each household (not to TAZs)
Previous tours affect number of subsequent
Essentially creating a travel diary

## Slide 15: Tour Purposes
Similar to four-step model but are prioritized:
    HBSchool
    HBU
    HBW
    HBShop
    HBOther
At-work after Destination Choice
No NHB
Purposes are interrelated in a household
More important purposes influence less important ones

## Slide 16: MRM25 Versions -- Each uses the same core model and land-use data
MRM25v1.0
For RFATS’ 2055 MTP
Model Runs Submitted for Conformity Determination January 2025
MRM25v2
For NC’s 2026-2035 STIP
Model Runs Submitted for Conformity Determination June 2025
MRM25v3
For NC’s 2055 MTPs
Model Runs Submitted for Conformity Determination October 2025

## Slide 17: MRM25 Validation
Region |  |  |  |  | 
Functional Class | # counts | Average Count | Average Assn | Assn/Cnt | RMSE
Freeway | 308 | 48,489 | 51,975 | 1.07 | 18
Expway | 49 | 32,176 | 37,421 | 1.16 | 33
Tfare | 2,823 | 13,087 | 12,530 | 0.96 | 34
Other | 693 | 2,941 | 2,350 | 0.80 | 73
All Facilities | 3,873 | 14,328 | 14,160 | 0.99 | 33.14
Volume Group | # counts | Average Count | Average Volume | Vol/Cnt | RMSE
<1,000 | 264 | 629 | 1,094 | 1.74 | 220.16
1,001-2,500 | 459 | 1,762 | 2,139 | 1.21 | 96.52
2,5001-5,000 | 556 | 3,747 | 4,213 | 1.12 | 68.04
5,001-10,000 | 847 | 7,436 | 7,422 | 1.00 | 43.29
10,001-25,000 | 1,239 | 16,093 | 14,924 | 0.93 | 29.42
25,001-50,000 | 499 | 34,253 | 33,981 | 0.99 | 23.64
>50,000 | 152 | 66,796 | 69,427 | 1.04 | 14.75
Total | 4,016 | 14,079 | 13,920 | 0.99 | 33.49

## Slide 18: MRM Other Uses -- CRTPO 2055 MTP – Project Ranking

## Slide 19: MRM Other Uses -- CRTPO 2055 MTP – Scenario Planning

## Slide 20: MRM Other Uses -- Accessibility

## Slide 21: Next Steps
Land-use updates (begin late 2026)
External model updates
Incorporating new CATS on-board ridership survey
Continued sensitivity testing & validation work
Managed lanes/tolling update?
Next model base year will be 2026

## Slide 22: For More Information:
Martin Kinnamon, PE
Program Manager
Metrolina Regional Model
martin.kinnamon@charlottenc.gov
(980) 721-8273