## Slide 1: COVID-19 Impacts on North Carolina Traffic
Kerry Morrow, NCDOT Traffic Survey Group
December 2, 2020

## Slide 2: Welcome
A strategic transportation plan connecting communities across North Carolina, focused on creating a more responsive, diverse, and inclusive transportation system for keeping people and freight moving safely and efficiently.
Today’s Presentation
Impacts to 2020 data collection
COVID-19 timeline
NC travel trends
How will it impact 2020 data analysis?
2021 data collection plans

## Slide 3
COVID-19 Impacts on North Carolina Traffic
2020 Data Collection
Factors:
Traffic monitoring program consists of ~53,000 data collection stations
NCDOT cash balance was very low; no overnight travel allowed
Uncertainty regarding safety
HR provisions
Impacts:
Stopped short-term data collection for 7 weeks from mid-March to end of May 2020
Resumed with limited productivity
Significant cuts in short-term data collection for 2020

## Slide 4
COVID-19 Impacts on North Carolina Traffic Traffic
2020 Data Collection
Collection priorities:
Safety – Top Priority
No overnight lodging
  Minimum number of stations collected
  More day trips
Gathering a sample of stations
  Primary Routes (US & NC)
    Collect once
      While school is out of session
    Collect a second time if possible
      While school is in session
  Secondary Routes & some Local Routes
    Collect to provide additional analysis as needed
Cancel collections that can be postponed and/or can be estimated
  Canceled Blue Ridge Parkway Collection
  Canceled Interstate/Freeway Ramp Collection

## Slide 5
COVID-19 Impacts on North Carolina Traffic
2020 Data Collection
Short-term Volume Collection
  24,275 stations scheduled for 2020
    Pneumatic tube counters, 48-hour counts
    Replaced with sample of ~7,000 stations
Short-term Class Collection
  1,033 stations scheduled for 2020
    Pneumatic tube counters, 48-hour counts
    No adjustments made

## Slide 6
COVID-19 Impacts on North Carolina Traffic
2020 Data Collection
Interstate Collection
  80 stations
    Temporary radar installed for 7-day counts
    Reduced to 47 stations
  2,921 ramp stations
    Pneumatic tube counters, 48-hour counts
    No ramps collected in 2020
    Will utilize factoring to perform ramp analysis with mainline control collections
Continuous Collection
  100 locations in NC (24/7/365)
    Permanent Radar, no interruptions in collection
    Will utilize data set for factoring other collected data sets

## Slide 7: COVID-19 Timeline Key dates for COVID-19 mitigation in North Carolina
COVID-19 Impacts on North Carolina Traffic
2020
March | April | May | June | July | August | Sept | Oct
March 10 Emergency Declaration
March 14 Public Schools Closed
March 17 Bars & Restaurants Closed
March 30 Stay at Home Order
May 8 Phase 1 Reopening
May 22 Phase 2 Reopening
September 4 Phase 2.5 Reopening
October 2 Phase 3 Reopening

## Slide 8
North Carolina Travel Trends
North Carolina
Travel Trends

## Slide 9: Travel Trend Reporting
NCDOT Leadership asked for weekly reporting of travel trends
Trends based on Continuous Count Stations
Data now on NCDOT dashboard (except VMT)
COVID-19 Impacts on North Carolina Traffic
NCDOT Continuous Count Stations
Notes: As of last week, this data is available on the NCDOT dashboard.
This map shows our 100 continuous site locations in NC. As you can see, we have them spread (albeit a little unevenly) in urban and rural areas. We are working on installing more continuous sites to provide a richer data set.

## Slide 10: Volume Trend – Weekly Change
Weekly Change: Average of daily changes from Pre COVID volumes
COVID-19 Impacts on North Carolina Traffic
March
May
July
September
April
June
August
October
2020

## Slide 11: Volume Trend – Day of Week
Compares day of week impacts for selected weeks
COVID-19 Impacts on North Carolina Traffic

## Slide 12: Volume Trend – Type of Route
COVID-19 Impacts on North Carolina Traffic

## Slide 13: Travel Trend – Based on VMT
A statistic used to measure travel is Vehicle Miles Traveled (VMT), generated by multiplying the length of a highway segment with its volume.
2018 VMT stats:
US VMT was about 3.3 Trillion
NC VMT was about 121 Billion
Average monthly NC VMT was about 10 Billion
VMT varies by Day of Week
Lowest travel day in NC is typically Sunday around 300 Million
Highest travel day in NC is typically Friday around 420 Million
Statewide Daily VMT will vary due to seasonal variation, holidays, adverse weather, and major events.
COVID-19 Impacts on North Carolina Traffic

## Slide 14: Travel Trend – Monthly
As of end of October, we have 16 Billion less VMT than forecasted
COVID-19 Impacts on North Carolina Traffic

## Slide 15: How will it impact 2020 Data Analysis?
COVID-19 Impacts on North Carolina Traffic
HPMS Deadline June 15, 2021
FHWA guidance
Pre-COVID-19 collected counts and prior year data can be used for comparison
Look at best practices from peer states in figuring out adjustment factors to annualize data
Bottom line: 2020 will have significantly higher number of stations with estimated counts than other years

## Slide 16: 2021 Data Collection Plans
COVID-19 Impacts on North Carolina Traffic
Travel will still be impacted by COVID-19
Anticipating possible new mitigation controls
Not anticipating new HR provisions
Planning for more data collection, less need to apply adjustment factors
Anticipating (hoping!) 2021-2022 schoolyear will be back to normal

## Slide 17
COVID-19 Impacts on North Carolina Traffic
Questions? Contact us!
Kerry Morrow
NCDOT Traffic Survey Group Supervisor
kmorrow@ncdot.gov
Kent Taylor
NCDOT Traffic Data Resource Engineer
kltaylor@ncdot.gov
Thank you!