## Slide 1: DCHC’s Performance Measure (PM) Tool
Yanping Zhang
2023 Fall NCMUG Meeting, Nov. 15th, 2023

## Slide 2
Introduction
Generating Performance Measures (PMs), Summary Report and Evaluating Scenarios
Supporting Metro Transportation Plan (MTP), Congestion Management Process (CMP), other programs and projects
Requiring Inputs & Outputs of Triangle Region Model (TRM) and/or Other Data Resources as inputs to the PM Tool
GISDK Script

## Slide 3
Geographical Levels
Performance Metrics are generated for three geographical levels
County, MPO & Region
Corridor & Transit Line
Link, Node, Stop & TAZ

## Slide 4
Summary Report – Part 1
Part 1 includes,
VMT
VHT
Average Speeds
Person Trip Length

## Slide 5
Summary Report – Part 2
Part 2 includes,
Commercial Vehicle (CV) Trip Length
Truck Trip Length
%VMT Experiencing Congestion (V/C ration>1)

## Slide 6
Summary Report – Part 3
Part 3 includes,
Mode Share by trip purpose and time of day
CV and Truck Trips
Population & Employment
Transportation Supply, highway lane miles

## Slide 7
Summary Report – Part 4
Part 4 includes,
Transit Ridership (unlinked Trips) by Transit Agency
Population & Employment
Supply Data, Transit Service Miles
Ridership of key transit routes

## Slide 8
Vehicle Miles/Hours Traveled (VMT/VHT)
Calculation Method 1 - Summing up VMTs/VHTs of all links. Mostly used for Region, MPO, & County.
Calculation Method 2 – Multiplying Trips by average time/distance. For VMT, however, paths with same travel time may have different travel distances (see the picture for reference). This method is mostly for a small area and Person Miles Traveled (PMT)

## Slide 9
Average Travel Time Calculation
For Inter-MPO/Inter-County Trips, trip Production (P) end determines which MPO/County it belongs to.
Calculation employes the following data items,
  Production-Attraction (P-A) Trip Matrices by
  trip purposes and Time of Day (TOD)
  P-A/A-P Travel Time matrices by TOD
  P-A Time of Day factor Tables

## Slide 10
Equity Measures
Equity Measures by Mode
Example for Auto mode
Average Travel Time of Production-Attraction Trips
TAZ/Community of Concern (CoC) includes,
Local Income CoC
Minority CoC
ZeroCar CoC. (Measures in the Transit Measure Table)

## Slide 11
2045 MTP Alternative Analysis

## Slide 12: 2050 MTP Alternative Analysis

## Slide 13
Non-Motorized and Bus Trips of TAZs

## Slide 14
New Measure - Job Accessibility By Mode
Previous Job accessibility by mode: Simply count total jobs within 30 minutes by auto. But spatial availability is not considered.
New proposed Measure - Spatially available opportunities. Proportional job allocation by workers/population
Job Accessibility by Auto of TAZ i= ()/ ()
* : Jobs of and
* n: total number of TAZs Whitin 30-minutes of TAZ i

## Slide 15
New Measure 2 – Travel Time Reliability
MAP-21 Performance Measures
Travel Time Reliability (TTR) by Interstate
and Non-Interstate National Highway
Estimate TTR and Level Of TTR (LOTTR) based on the TRM output and Base year INRIX travel speed information.

## Slide 16
Thank You