## Slide 1: Guidance on Considering CAVs in Travel Demand Models (NCDOT RP 2023-11)
NCMUG Spring Meeting
Leta Huntsinger, PhD, PE | WSP
Si Shi, MCRP | ITRE

## Slide 2: Research Goals
Investigate the consideration of Connected and Automated Vehicles (CAVs) in Travel Demand Models (TDMs) supported with case study analysis.
Develop guidelines that NCDOT and MPOs can use to inform the modification and application of TDMs to include CAVs.

## Slide 3: Acknowledgements
Steering and Implementation Committee
Jaehoon Kim, Research Engineer
Research Team
Leta Huntsinger, Principal Investigator
Graphic Designer
Lisa Callister
Joe Hummer, Project Champion
Alena Cook
Keith Dixon
Tae-Gyu Kim
Travis Marshall
Si Shi
Fahim Kafashan
Ali Hajbabaie
Shoaib Samandar
Vince Bernardin
Kyle Ward

## Slide 4: Index of Predictions and Factors

## Slide 5
Strategic Scenario Planning
Approach
Case Study Evaluation
Findings & Recommendations
Q & A

## Slide 6: Strategic Scenario Planning

## Slide 7: Strategic Scenario Planning
Research driving forces
Determine patterns of interaction
Create scenarios
Analyze implications
Evaluate scenarios
Provides an analytical framework and process for understanding complex issues and responding to change
Facilitates consensus building by giving communities the capacity to participate actively in planning
Includes tools and techniques to assess the impact of transportation and other public policy choices on a community
Allows the opportunity to recognize the impact of tradeoffs among competing goals
https://highways.dot.gov/public-roads/septemberoctober-2005/scenario-planning

## Slide 8: Approach

## Slide 9: Multi-Tiered Approach

## Slide 10: Approach: Tier 1
Existing Model Design

## Slide 11: Adjust Existing Model Parameters
Parameter Adjustment | Sub-category | Scenarios | 
 |  | Medium-High (70%) | High (95%)
Value of Time | All people1 | -60% | -65%
Trip rates | All purposes2 | 9% | 15%
Highway Capacity | Signalized arterial | 40% | 70%
 | Control access facility | 47% | 77%
1 The reduction applied in the model reflects the recommended reduction multiplied by the expected CAV adoption rate for the scenario. For medium-high scenario, VOT should be reduced by 42% (60%*70%).
2The adjustment captures additional trips resulting from ease of travel with CAVs, increased accessibility for elderly and disabled people, and empty trips from car sharing among household members.

## Slide 12: Approach: Tier 2
Model Design Changes

## Slide 13: Conceptual Framework

## Slide 14: Conceptual Framework

## Slide 15: Approach: Scenario Development
Tier 2 - Model Design Changes

## Slide 16: Model Design
* Trip purpose specific

## Slide 17: Performance Measures
System Level
Average trip length by purpose
Project Level
Demand
Vehicle miles traveled (total and congested)
Delay
Capacity
Demand-to-capacity ratio
Daily delay
Daily delay per mile

## Slide 18
P# | Facility Type | Project Type | Roadway Name
1 | Interstate | Widening | I-40
2 | Freeway | New Location | NC 540
3 | Freeway | Widening | US 1
4 | Freeway | Widening | US 1
5 | Arterial | Widening | NC 50
6 | Arterial | Widening | NC 42
7 | Rural Roadway | New Location | Chatham Parkway

## Slide 19: Case Study Evaluation

## Slide 20: Evaluation Approach
Implement model design changes (model design scenario only)
Adjust parameters
Run model
2050 build – no CAVs
2050 build – CAVs (MH and H)
2050 no build – CAVs (focus on project level evaluation, MH only)
Summarize and evaluate results

## Slide 21: Case Study Evaluation TRM Model Design Results
System Level Metrics
Assumption: Level 5 automation

## Slide 22
CAVs lead to a longer average trip length (mi) for all trip purposes.
The biggest impact is for interim stops on a work tour and long duration discretionary trips, reflecting the influence of the changes in the asserted coefficients.
K-12 trips are least impacted by CAVs.
Trip Purposes
P1: Work tour
P2: Work tour – interim stop
P3: Work tour – drop kids at K12
P4: K12 trips
P5: Shop, dine, other trips
P6: Long duration discretionary trips
P7: Short duration discretionary trips
P8: Medical trips

## Slide 23
CAVs increase VMT with greater increases for the high scenario.
Overall VMT increases, but congested VMT decreases.
This is a direct reflection of the capacity benefits resulting from CAVs.

## Slide 24
Delay decreases for all facility types, with the largest reductions in delay for freeways and multilane highways.
This is a direct reflection of the capacity benefits resulting from CAVs.

## Slide 25: Case Study Evaluation TRM Model Design Results
Project Level Metrics – Medium High CAV Scenario
Assumption: Level 5 automation

## Slide 26: Project 1 I-40 Widening
CAVs offer benefits in both the build and no build scenario.
The benefits of CAVs are like those seen when we build the project. Depending on the target D/C ratio, this could suggest delaying the project, but the presence of CAVs do not overcome the need for the project at MH adoption levels.
 | Build No CAV | Build MH CAV | No Build MH CAV
Capacity | 12,329 | 18,124 | 12,083
Demand (peak hour) | 8,473 | 10,165 | 9,891
D/C | 0.69 | 0.56 | 0.82
Cost of delay per mile with project but no CAVs | $ 114
Cost of delay per mile with project and CAVs | $ 31
Savings | $ 82
Cost of delay per mile with CAVs but no project | $ 139
Loss | $ (26)

## Slide 27: Project 3 US 1 Widening
CAVs offer benefits in both the build and no build scenario.
The benefits of CAVs are not enough to overcome the need for the project.
 | Build No CAV | Build MH CAV | No Build MH CAV
Capacity | 12,277 | 18,048 | 12,032
Demand (peak hour) | 12,555 | 15,333 | 14,458
D/C | 1.02 | 0.85 | 1.20
Cost of delay per mile with project but no CAVs | $ 147
Cost of delay per mile with project and CAVs | $ 88
Savings | $ 59
Cost of delay per mile with CAVs but no project | $ 322
Loss | $ (175)

## Slide 28: Case Study Evaluation Sensitivity Testing

## Slide 29: Project 1 I-40 Widening
The effect on system-level delay to changes in land use patterns and trip making is very small.
The capacity variable shows a higher degree of risk with a 40% higher measure of systems delay for the cautious capacity values.
Range of Uncertainty as Measured by Delay

## Slide 30: Project 1 I-40 Widening
The effect on system level peak period VMT to changes in all variables is very small, suggesting lower levels of risk in the asserted values of these variables through the lens of systems level VMT.
Range of Uncertainty as Measured by Peak VMT

## Slide 31: Project 1 I-40 Widening
Peak period congested VMT shows a similar pattern as the daily delay.
Land use patterns and trip making having a small impact on congested VMT.
The degree of risk for the capacity variable is much higher.
Range of Uncertainty as Measured by Congested VMT

## Slide 32: Findings and Recommendations

## Slide 33: Findings
Significant contribution to the use of travel models in a strategic scenario planning context to better understand the potential effects of CAVs.
The tiered approach lays a solid groundwork for changes that could be implemented immediately as well as those that require more time and effort but offer more behavioral realism.
This work informed the development of guidelines that can be used to incorporate findings into the models to better capture the effects of CAVs on long range transportation plans, project prioritization and project level traffic forecasts.

## Slide 34: Recommendations
Immediately incorporate the consideration of CAVs in traffic forecasts and long-range transportation plans.
Incorporate model design changes for CAVs in future model development efforts.
Implement a regular practice of risk and uncertainty analysis.

## Slide 35: Thank You!