MINIMUM PROBLEM STATEMENT EXAMPLE

Shiloh Road (SR 2318),  Local ID: IRED0010-H

Shiloh Road (SR 2318) between Amity Hill Road (SR 1840) and the Statesville planning boundary is expected to be over capacity by 2030.  Improvements are needed to accommodate projected traffic in order to maintain a Level of Service “D”.  At the north end of Shiloh Road, bridge number 22 has been designated functionally obsolete by the NCDOT Bridge Maintenance Unit.

This section of Shiloh Road currently has a two-lane, 18-foot cross section.  The 2003 annual average daily traffic (AADT) is 2,000 vehicles per day (vpd); by 2030, the AADT is expected to be 11,300 vpd compared to a LOS “D” capacity of 11,000 vpd for the existing cross section.  Near the Shiloh Road and Amity Hill Road intersection there are plans for the construction of a new regional shopping complex on the east side of Troutman and Statesville which accounts for the high percent increase in traffic.  The CTP project proposal (Local ID IRED0001) is to provide a four-lane, boulevard facility with turn lanes where necessary.