## Slide 1: Movement-Based Safety Performance Functions
NCDOT Project 2022-13 Closeout Meeting
Chris Cunningham, PE
Ishtiak Ahmed
Richard Thomas Chase
James Poslusny
Kyra Stash
May 17, 2024

## Slide 2: Background
NCDOT RP 2018-20: Reasonable Alternatives for Grade-Separated Intersections
Limited dataset (35)
  21 Conventional
  11 RCUT
  3 DDI
Only used conflict point type and 24h movement volumes
Model was tested by NCDOT against 300+ Charlotte conventional intersections

## Slide 3: Safety Analysis - Methodology
Model Estimation Process
CP Types
Crossing
Merging
Diverging
Conflict Movement Volumes (CMVs)
= ∑AADT x TM (%)
CP Crashes
Frequency
Severity
NCP Crashes
Frequency
Severity
AADT Data
Major AADT
Minor AADT
Crash Data
Intersection Crash Frequency and Severity
Travel Directions of Related Vehicles
Vehicle Maneuvers of Related Vehicles
Crash Classification
CP-SPF
NCP-SPF
Model Estimation
Model Estimation
In addition to the classified CP/NCP crashes, the conflicting movement volumes (CMVs), CP types (cross/merge/diverge), and AADT data should be collected for model estimation.

## Slide 4: Safety Analysis - Methodology
Model Application Process
CP-SPF
NCP-SPF
AADTMinor
AADTMajor
Predict
Predict
CMVMajor
CMVMinor
Merging CP
In the applications, the CP- and NCP-SPFs predict the crashes separately, and then the predicted crashes are aggregated to the intersection-level total crashes.

## Slide 5: Safety Analysis - Methodology
Conflicting Movement Volumes (CMVs)
The CMVs are the two movement AADTs passing a conflict point
Like the traditional SPF, the CP-SPF uses major & minor CMVs as exposures
The major and minor CMVs are determined as follows. - Higher volume = Major CMV - Lower volume = Minor CMV
Conflict Point
Movement A
Movement B
Concept of CMVs
Intersection
Minor AADT
Major AADT
Conceptually
Similar
Traditional SPF

## Slide 6: Data Collection: Variables
Movement Volumes
Number and Type of Lanes
Posted Speed Limit
Relative Angle between movements
Traffic Control (Lefts)
Lateral Offset (Lefts)
RT Channelization
RTOR Allowed

## Slide 7
Predictor name | Type | Distribution | Potential use in model(s)
1. Movement-based volume | Numerical | - | All
2. Number of lanes by movement | Numerical | - | Crossing, merge, and diverge
3. Type of lane by movement | Categorical | All exclusive: 50% All shared: 39% Mix of shared and exclusive: 11% | Crossing, merge, and diverge
4. Posted speed limit | Numerical | - | All
5. Relative angle between two crossing movements | Categorical | Base: 81% Acute: 9% Obtuse: 10% | Crossing and merge
6. Left-turn control type | Categorical | Protected: 42% Permissive: 34% Protected-permissive: 24% | Crossing and merge
7. Left-turn lateral offset | Categorical | Base: 35% Positive: 21% Negative: 44% | Crossing
8. Right-turn channelized? | Categorical | Yes: 5% No: 95% | Merge and diverge
9. Right-turn on red allowed? | Categorical | Yes: 99% No: 1% | Merge and diverge

## Slide 8: Discussions
Crash Data Analysis Difficulties
  Skewed Intersections
  Non-Cardinal Intersections
  Multivehicle (3+)
  Turn bay-adjacent crashes (left or right)
Excluding sites and individual crashes vs. categorizing NCP
  Driveways
  Bike-Ped involved
  U-turns
  Lack of narrative detail for movement assignment

## Slide 9: Non-Cardinal Intersections
Cardinal
Non-Cardinal

## Slide 10: U-Turn Movements

## Slide 11: Driveways

## Slide 12: 3+ Vehicles

## Slide 13: N/S Misaligned in Crash Diagram

## Slide 14: Pedestrian Crash

## Slide 15: Incorrect use of lanes

## Slide 16: Methodology – Predictive Models
Negative Exponential (Poisson)
Negative Binomial
Hurdle Model

## Slide 17: NCP Models – Total Crashes
Variable | Estimate | P Value
Intercept | -11.4529 | <0.01
log(MajorVol) | 0.86102 | <0.01
log(MinorVol) | 0.50789 | <0.01
Max PSL > 35 mph | 0.16251 | <0.05
Variable | Estimate | P Value
Intercept | -12.25 | <0.01
log(MajorVol) | 0.93737 | <0.01
log(MinorVol) | 0.52196 | <0.01
AIC = 1652
AIC = 1654

## Slide 18: NCP Models – F/I and PDO
AIC = 1652
 | Fatal/Injury |  | PDO | 
Variable | Estimate | P Value | Estimate | P Value
Intercept | -11.4529 | <0.01 | -12.9832 | <0.01
log(MajorVol) | 0.86102 | <0.01 | 0.97716 | <0.01
log(MinorVol) | 0.50789 | <0.01 | 0.51099 | <0.01
Max PSL > 35 mph | 0.16251 | <0.05 | 0.37950 | <0.01
In CBD | -- | -- | 0.17126 | <0.05
AIC = 1164 | 1539
 | Fatal/Injury |  | PDO | 
Variables | Estimate | P Value | Estimate | P Value
Intercept | -13.7709 | <0.01 | -12.5122 | <0.01
log(MajorVol) | 0.97368 | <0.01 | 0.92423 | <0.01
log(MinorVol) | 0.49720 | <0.01 | 0.53354 | <0.01
AIC = 1172 | 1545

## Slide 19: Crossing Conflict Point Models – Total Crashes
Count Model |  | 
Variable | Estimate | P Value
Intercept | -7.1495 | <0.01
log(higher vol) | 0.30582 | <0.01
log(lower vol) | 0.37669 | <0.01
Skewed Combination | -0.92466 | <0.01
Not all Protected | 0.51311 | <0.01
Zero Hurdle Model |  | 
Variable | Estimate | P Value
Intercept | -10.3319 | <0.01
log(higher vol) | 0.73283 | <0.01
log(lower vol) | 0.36676 | <0.01
Skewed Combination | -0.45293 | <0.01
AIC = 6791

## Slide 20: Crossing Conflict Point Models – F/I and PDO
Count Model |  |  |  | 
 | Fatal/Injury |  | PDO | 
Variable | Estimate | P Value | Estimate | P Value
Intercept | -7.26278 | <0.01 | -6.75981 | <0.01
log(higher vol) | 0.35432 | <0.01 | 0.19764 | <0.05
log(lower vol) | 0.39995 | <0.01 | 0.37695 | <0.01
Skewed Combination | -1.02185 | <0.01 | -1.02481 | <0.01
Not all Protected | 0.49623 | <0.01 | 0.45817 | <0.01
Zero Hurdle Model |  |  |  | 
 | Fatal/Injury |  | PDO | 
Variable | Estimate | P Value | Estimate | P Value
Intercept | -10.8126 | <0.01 | -9.64337 | <0.01
log(higher vol) | 0.70315 | <0.01 | 0.60203 | <0.01
log(lower vol) | 0.36388 | <0.01 | 0.34004 | <0.01
Skewed Combination | -0.38555 | <0.01 | -0.59968 | <0.01
AIC = 4685 | 4893

## Slide 21: Crossing Conflict Point Models – Volume only
Variable | Estimate | P Value
Intercept | -8.8639 | <0.01
log(CMV higher vol ) | 0.58038 | <0.01
log(CMV lower vol) | 0.35987 | <0.01
AIC = 6959
 | Fatal/Injury |  | PDO | 
Variable | Estimate | P Value | Estimate | P Value
Intercept | -10.1449 | <0.01 | -8.93961 | <0.01
log(CMV higher vol ) | 0.63575 | <0.01 | 0.51771 | <0.01
log(CMV lower vol) | 0.37116 | <0.01 | 0.35321 | <0.01
AIC = 4767 | 4981

## Slide 22: Diverge Conflict Point Models
Variable | Estimate | P Value
Intercept | -8.3855 | <0.01
log(CMV higher vol ) | 0.32842 | <0.01
log(CMV lower vol) | 0.34888 | <0.01
AIC = 1453
 | Fatal/Injury |  | PDO | 
Variable | Estimate | P Value | Estimate | P Value
Intercept | -9.39924 | <0.01 | -8.73796 | <0.01
log(CMV higher vol ) | 0.2819 | 0.1201 | 0.33622 | <0.01
log(CMV lower vol) | 0.3123 | <0.05 | 0.35978 | <0.01
AIC = 442 | 1267

## Slide 23: Merge Conflict Point Models
Variable | Estimate | P Value
Intercept | -7.3265 | <0.01
log(CMV higher vol ) | 0.34698 | <0.01
log(CMV lower vol) | 0.30371 | <0.01
AIC = 2431
 | Fatal/Injury |  | PDO | 
Variable | Estimate | P Value | Estimate | P Value
Intercept | -9.38636 | <0.01 | -7.54544 | <0.01
log(CMV higher vol ) | 0.51276 | <0.01 | 0.30230 | <0.01
log(CMV lower vol) | 0.17908 | <0.05 | 0.35373 | <0.01
AIC = 953 | 2084

## Slide 24: Tool Application

## Slide 25: Tool Application (outputs)

## Slide 26: Fatal + Injury vs PDO
HSM has intersection-total models for PDO and F/I separately, and adds them up for total crash estimates
MBSPF has 33 models (32 CP and 1 NCP for 4SG) per intersection, so fitting F/I on mostly zeroes at conflict point models
How to implement?
  Estimate total then use estimated %: F/I = Total model * F/I model / (F/I model + PDO model)
  Estimate like HSM: Total = PDO model + F/I model
  Estimate with default %: F/I = Total model * %F/I

## Slide 27: Overall Model Performance
Cumulative Residuals (CURE)
Chart: Major AADT
Chart: Minor AADT

## Slide 28: Overall Model Performance
Chart: MBSPF vs HSM Crash Estimates (all Charlotte sites)

## Slide 29: Overall Model Performance
Test dataset: 25% Charlotte Sites (not modeled) and 15 Cary Sites
Used Volume-Only MBSPF Total Crash Models and HSM with all geometric and control factors
Root Mean Squared Error (RMSE) and Mean Absolute Percentage Error (MAPE)
RMSE (Test) |  | MAPE (Test) | 
MBSPF | HSM | MBSPF | HSM
6.1 | 13.2 | 46.5% | 87.3%

## Slide 30: Next Steps
Incorporate StIC comments into Final Report
Use of MBSPF in ongoing work
MBSPF future research
  Unsignalized: Two-way/Four-way, Leftover, U-turn
  RBT Merge and Diverge
  Major-Major Crossover
  U-turn Merge and Diverge