RESURFACING EXISTING BRIDGES:

| (7-1-95) (Rev. 8-21-12) |  | SP6 R61AR |
| --- | --- | --- |

The Contractor's attention is directed to the fact that he will be required to resurface the bridges on this project if directed by the Engineer.

Place the surface so as to follow a grade line set by the Engineer with the minimum thickness as shown on the sketch herein or as directed by the Engineer.  State Forces will make all necessary repairs to the bridge floors prior to the time that the Contractor places the proposed surfacing.  Give the Engineer at least 15 days notice prior to the expected time to begin operations so that State Forces will have sufficient time to complete their work.

At all bridges that are not to be resurfaced, taper out the proposed resurfacing layer adjacent to the bridges to insure a proper tie-in with the bridge surface.