TRENCHING FOR INTERMEDIATE COURSE:

| (7-1-95) (Rev. 8-21-12) | 610 | SP6 R79BR |
| --- | --- | --- |

Perform all trenching necessary to place the asphalt concrete intermediate course widening in accordance with the typical sections, at locations shown on the sketch maps, and as directed by the Engineer.

Perform the trenching for the intermediate course on the same day that the intermediate course is to be placed.  If the intermediate course cannot be placed on the same day the trench section is excavated, backfill the trench with earth material and compact it to the satisfaction of the Engineer.  Once the trench is open, perform backfilling and re-opening of the trench at no cost to the Department.

The Contractor will be restricted to widening one side of the project at a time unless otherwise permitted by the Engineer.  In widening, operate equipment and conduct operations in the same direction as the flow of traffic.

Density tests may be taken every 2,000 feet in the widened areas as directed by the Engineer.  Shape and compact the subgrade in the widened areas to the satisfaction of the Engineer.  Compact the asphalt concrete intermediate course in the widened areas in accordance with the provisions of Article 610-9 of the 2012 Standard Specifications.

Place the excavated material from trenching operation on the adjacent shoulder area as directed by the Engineer.  Cut adequate weep holes in the excavated material to provide for adequate drainage as directed by the Engineer.  Remove all excavated material from all drives to provide ingress and egress to abutting properties and from in front of mailboxes and paper boxes.  Saw a neat edge and remove all asphalt and/or concrete driveways, and existing asphalt widening, as directed by the Engineer, to the width of the widening and dispose of any excavated concrete or asphalt materials.  Properly reconnect driveways.

Upon completion of the paving operation, backfill the trench to the satisfaction of the Engineer.  Properly dispose of any excess material remaining after this operation.

No direct payment will be made for trenching, sawing, and removal of driveways, depositing material on shoulder area, backfilling trench, or removal of spoil material, as the cost of this work shall be included in the bid unit price per ton for Asphalt Concrete Intermediate Course, Type ___.