## Slide 1: Diverging Diamond Interchange
NORTH CAROLINA DEPARTMENT OF TRANSPORTATION
Notes: Presentation is designed to provide an overview of a new design alternative being considered by NCDOT called the Diverging Diamond Interchange.

## Slide 2
The diverging diamond interchange known as a DDI is designed to allow two directions of traffic to temporarily cross to the opposite side of the roadway to provide easier access on and off the freeway.
What is a Diverging Diamond Interchange?
FEATURES
Limits number of traffic signal phases required to move motorists through the interchange
Movements on and off of the freeway have fewer conflict points and can be free-flowing
Moves high volumes of traffic without increasing the number of lanes in an interchange
Notes: 2
Slide should provide general information about the DDI.

## Slide 3
Where are Diverging Diamond Interchanges?
  France
History
Autoroute de Normandie (Highway A13) avec Boulevard de Jardy, Versailles, France
Notes: First DDI was constructed in France. This photo is one of three DDI type interchanges constructed in that country.

## Slide 4
Where are Diverging Diamond Interchanges?
  France
  USA
History
US 60 in Springfield, Missouri
I-15 in American Fork, Utah
Notes: The DDI concept was first introduced to the States in 2003 by a civil engineer from Maryland named Gilbert Chlewicki. He saw that many traditional diamond interchanges were over capacity and in need of improvements.
Missouri Department of Transportation (MoDOT) constructed the first DDI in the USA in Springfield, Missouri during the Summer of 2009. This interchange was a conversion of an existing standard diamond interchange. The MoDOT has constructed one more in Springfield, another in St. Louis and plans to build additional DDIs.
This type of interchange is being designed/studied for use in California, Georgia, Florida, Illinois, Kentucky, Maryland, New York, Ohio, Oregon, Rhode Island, and Tennessee, Utah and Virginia. One in Utah and another in Tennessee were opened to traffic in 2010, and one in New York should be completed in 2011.

## Slide 5
What are the Benefits?
  Fewer conflict points (18 for DDI, 30 for conventional)
  Better sight distance at turns
  Wrong way entry to ramps extremely difficult
  Less horizontal curvature reduces risks of off-road crashes
  Virtually no driver confusion (FHWA study)
  Simple left and right turns from all directions
  Increases left turn lane capacity without adding lanes
  Two phase signals with shorter cycle lengths reduces delay
  Better storage between the ramp terminals
  Safety
  Operations
Notes: The DDI has numerous benefits when compared to other design alternatives.

## Slide 6
What are the Benefits?
  For a retrofit
    Existing bridge can usually be used
    Additional right-of-way rarely needed
    Construction time is reduced
    Requires minimal detouring during construction
  For a new interchange
    Usually requires less lanes than other interchange types
    Less bridge structure
    Less right-of way than a cloverleaf
  Costs
Notes: The DDI has been shown to provide a significant cost savings over other design alternatives.
For retrofit projects, a DDI often can be constructed using the existing bridge and inside the existing right-of-way. Because many of the existing interchange features can remain intact, the DDI is often constructed in a fraction of the time of a new interchange.
MoDOT was able to construct the first Springfield DDI in less than six months, while maintaining traffic at the location.

## Slide 7
How Does it Operate?
Video courtesy of Missouri DOT
Notes: This is aerial footage taken by news in Missouri when the DDI opened. The interchange was actually still under construction. The concrete islands at the ramps had not been completed.

## Slide 8
The DDI is considered an “unconventional design”. Without accurate information many assume a DDI will:
Common Concerns
  Cause driver confusion
  Encourage wrong way moves
  Slows down traffic
  Cannot accommodate bikes, trucks, pedestrians or emergency vehicles
Notes: The DDI concept is still fairly new to the public, so we anticipate that many may have concerns and worries about how the interchange will operate. Which is why, of course, we developed this presentation to provide accurate information about DDIs. These items are probably the most frequently heard from the public.

## Slide 9
Driver Expectations
Photos courtesy of FHWA Publication No. FHWA-HRT-07-048
  Additional signage, lighting, and pavement markings may be needed to reinforce correct driving patterns
  Glare screen (if necessary) blocks headlights of opposing traffic
Notes: The following design elements are encouraged by the Federal Highway Administration to reduce driver confusion.
Proper pavement markings and signs inform drivers of the restricted movements.
Additional lighting may be needed to increase visibility at night. However, this is true of most interchanges.
Glare screen are also an option to shield the headlights of opposing traffic at the signals where needed. It was found after the first few DDIs were constructed that glare screens were not needed at those locations.

## Slide 10
Bikes/Trucks/Emergency Vehicles
  DDI has been designed to accommodate trucks
  Access for fire trucks, EMS vehicles is no different than standard diamond interchange
  Wide outside lane (14 ft.) or separate bike lane can be provided.
Image courtesy of Missouri DOT
Notes: DDIs are designed to accommodate large vehicles that require greater turning radii as they travel through the interchange. The plans show the path a truck would take in each lane. You can also see that through the curves, the lanes are wider to account for a larger vehicle.

## Slide 11
Pedestrians
Notes: The DDI is unique in that pedestrians are given a true refuge area to walk from one end of the interchange to the other. This pedestrian path is located in the center of the bridge. This design file snapshot shows the marked crossings and center pedestrian island. It appears that the center island concept has fewer conflicts for pedestrians, and should prove to be safer.

## Slide 12
Pedestrians
  Protected pedestrian crossing can be provided at signal
  Pedestrian refuge area is provided in concrete median/islands
  Decreased exposure to free-flowing turning movements
Notes: Here’s pictures of the center pedestrian walkway in Springfield. The side walls provide a positive barrier between vehicular movements and pedestrians, but is not too tall to provide a “tunnel” effect that could compromise pedestrian security.

## Slide 13
Proposed North Carolina DDI Projects
  Asheville I-26 at NC 280 (Asheville Airport)
  Concord I-485 at Mallard Creek Road
  I-85 at Poplar Tent Road
  I-85 at NC 73
  I-85 at US 29-601
  Cornelius I-77 at Catawba Avenue
  Kernersville I-40 at Union Cross Road
  Lumberton I-95 at US-301 (Fayetteville Road)
  Leland US 17 at NC 133 (River Road)
Notes: Here is a list of some of the locations where DDIs are being planned and designed for construction in North Carolina.

## Slide 14
Asheville: I-26 at NC 280
Notes: Here’s a couple of locations where NCDOT has identified DDIs as solutions to existing traffic problems. The first one is next to the Asheville Airport on I-26. Heavy left turns to and from the interstate cause delays and backups. You can see from this recent aerial photo that the local Division has widened and lengthened the off ramp coming from Asheville. Even with these improvements, there are still significant delays, and with future growth in the area, those delays and queues will increase.

## Slide 15
Asheville: I-26 at NC 280
Level of Service Comparison
Notes: We analyzed the operation of the interchange, both “as is” and as a diverging diamond. Here’s a level of service chart for both existing volumes, and projected 2025 volumes. The existing interchange currently operates at LoS D and E, with significant queuing. In 2025, almost all movements are a poor LoS F, with major backups.
With the DDI, operation today would be LoS B, and in 2025, still either a B or C, with minimal queuing on NC 280, but no problems on the I-26 ramps. A huge improvement, without needing to widen ramps or the bridge.

## Slide 16
US 17 at NC 133 (River Road)
Leland, Brunswick Co.
Notes: This interchange exists as a traditional diamond. Significant traffic growth has occurred in the Wilmington area, particularly in Leland, and the volumes exceed the available capacity for the interchange.

## Slide 17
US 17 at NC 133 (River Road)
Notes: When the project was reviewed in 2007 the original recommendation was to redesign the interchange to include a loop ramp in the southeast quadrant. Right of way estimates came back nearly $12 Million dollars over budget to make the improvements. We were asked to take another look at this interchange and see if what improvements could be made without significant ROW costs.

## Slide 18
US 17 at NC 133 (River Road)
Level of Service and Delay 2035 |  | Traditional Diamond |  | Partial Cloverleaf |  | DDI | 
 |  | LOS | Delay | LOS | Delay | LOS | Delay
NB Ramp | NB Left | F | 225.8 | C | 29.4 | C | 31.0
 | NB Right | E | 68.4 | B | 19.8 | C | 16.6
 | EB Left | F | 208.9 | - | - | - | -
 | EB Thru | A | 5.4 | B | 12.3 | D | 47.1
 | WB Thru | C | 31.6 | D | 53.9 | C | 33.6
 | WB Right | F | 243.6 | - | - | - | -
SB Ramp | SB Left | F | 88.1 | F | 84.3 | D | 39.9
 | SB Right | F | 92.5 | F | 87.7 | E | 55.7
 | EB Thru | F | 106.5 | F | 172.5 | F | 86.7
 | EB Right | C | 32.8 | C | 34.2 | - | -
 | WB Left | C | 29.3 | F | 102.4 | - | -
 | WB Thru | C | 22.4 | D | 37.6 | D | 37.3
Notes: The chart provides comparison of the alternatives considered. Alternative A was essentially a no-build alternative. It only included minor ramp improvments, but did nothing to increase capacity on River Road. The Loop Alternative showed improve ove rthe existing condition but still had several movements with poor LOS. The solution was the DDI. Not only did our analysis show it out performed the diamond and partial cloverleaf designs, it also could be constructed within the existing ROW.

## Slide 19
Image courtesy of Fisher Associates, Inc.
US 17 at NC 133 (River Road)
  Proposed lane crossings will be under the bridge structure
  No right-of-way claims with adjacent property owners
Notes: This is a visual rendering of a DDI that goes under the freeway bridge. This simulation was created for a project in New York and is similar to what is being proposed at the US 17 and NC 133 (River Road) interchange.

## Slide 20
US 17 at NC 133 (River Road)
Alternative B: Partial Cloverleaf
  Right of Way: $11,875,000
  Construction: $19,400,000
  Utilities: $476,335
  Total $31,751,335
Alternative C: Diverging Diamond
  Right of Way: $1,875,000
  Construction: $17,650,000
  Utilities: $476,335
  Total $20,001,335
Cost estimates include bridge and corridor widening work as well as interchange reconfiguration.
Notes: The cost breakdown for each alternative is shown here. You can see that the DDI saves 10 Million dollars in right-of-way costs. Note that the costs listed are for the entire project, not just the interchange.

## Slide 21
Cornelius, Mecklenburg Co.
I-77 at Catawba Avenue
Notes: The proposed DDI in Cornelius at I-77 and Catawba Avenue is scheduled to be one of the first constructed in the State. Construction is scheduled for 2013.
The existing interchange has a high crash rate and chronic left-turn back-ups. You can see that there is quite a bit of commercial development, driveways and adjacent intersections in close proximity of the ramps.
The lack of access management at this location limits the available right-of-way needed for constructing lane and ramp improvements. The DDI alternative allows the interchange to operate better than the existing condition, without adversely impacting any property owners. As with a traditional diamond interchange, improvements to the intersections close to the interchange will still be needed in order for the corridor to function well.

## Slide 22
Cornelius, Mecklenburg Co.
I-77 at Catawba Avenue
Notes: The proposed DDI in Cornelius at I-77 and Catawba Avenue is scheduled to be one of the first constructed in the State. Construction is scheduled for 2013.
The existing interchange has a high crash rate and chronic left-turn back-ups. You can see that there is quite a bit of commercial development, driveways and adjacent intersections in close proximity of the ramps.
The lack of access management at this location limits the available right-of-way needed for constructing lane and ramp improvements. The DDI alternative allows the interchange to operate better than the existing condition, without adversely impacting any property owners. As with a traditional diamond interchange, improvements to the intersections close to the interchange will still be needed in order for the corridor to function well.

## Slide 23
Cornelius, Mecklenburg Co.
I-77 at Catawba Avenue
Notes: The proposed DDI in Cornelius at I-77 and Catawba Avenue is scheduled to be one of the first constructed in the State. Construction is scheduled for 2013.
The existing interchange has a high crash rate and chronic left-turn back-ups. You can see that there is quite a bit of commercial development, driveways and adjacent intersections in close proximity of the ramps.
The lack of access management at this location limits the available right-of-way needed for constructing lane and ramp improvements. The DDI alternative allows the interchange to operate better than the existing condition, without adversely impacting any property owners. As with a traditional diamond interchange, improvements to the intersections close to the interchange will still be needed in order for the corridor to function well.

## Slide 24
I-77 at Catawba Ave.
  For a SPUI
    ~$30 Million
  For a DDI
    ~$3.5 Million
Cost Estimates
Notes: The original proposal at this interchange was to construct a Single Point Urban Interchange (SPUI.) Construction and Right-of-way estimates were about $30 million. This type of interchange is expensive because of the more substantial bridge structure, and construction of that bridge while still maintaining traffic operations at the interchange. Because the DDI can use the existing bridge structure, costs are about a tenth of the other estimate. And the DDI provides better traffic operations than the SPUI.

## Slide 25
Summary
  The DDI has shown great potential for improving conditions for many interchanges
  The DDI can reduce overall construction time and save money
  Operation of adjacent signals intersection may affect DDI effectiveness
  The DDI as an “unconventional design” may become as commonplace for interchanges as the roundabout for intersections, especially in place of SPUI designs
  The DDI is not a silver bullet solution but it has many applications worth exploring for certain interchange
Notes: Summary

## Slide 26
For More Information Contact:
Congestion Management Section
Transportation Mobility and Safety Division
North Carolina Department of Transportation
1561 Mail Service Center
Raleigh, NC 27699-1561
Phone: (919) 773-2800
Notes: Contact information.