## Slide 1: Superstreets “A Tool for Safely and Efficiently Managing Congestion”
Original Presentation Prepared for
NORTH CAROLINA DEPARTMENT OF TRANSPORTATION
TRANSPORTATION MOBILITY AND SAFETY DIVISION
By
Stantec Consulting Services Inc.
Notes: Good morning and Welcome!
Before I begin, I want to take this opportunity to thank you for coming and welcome you on behalf of the North Carolina Department of Transportation to our presentation on the "superstreet". We are really excited to be here today to share one way your Department of Transportation is addressing the needs of our State's transportation system and leading the country in innovative design techniques.
The superstreet concept refers to a reconfiguration of the traditional intersection. This idea has been used in different parts of the country to alter traffic flow when safety and delay at intersections would benefit from its use. The North Carolina Department of Transportation has supported the development of a “new” application of the superstreet that was implemented on a section of roadway near Leland, North Carolina along US 17 in 2007. This application was considered to be the first signalized superstreet in the nation. Today, we have plans to apply this concept to locations across the State. Thus, the superstreet is now considered a new tool in the Department of Transportation’s tool box. It is a means to relieve the effects of congestion along our roadways and protect our environment by improving air quality along congested corridors. As an added bonus, it can significantly reduce the cost of construction to roadway projects that might otherwise require large interchanges to handle traffic demands.

## Slide 2: NC Department of Transportation
Mission Statement
“Connecting people and places in North Carolina - safely and efficiently with accountability and environmental sensitivity.”
Notes: Our core goal at the North Carolina Department of Transportation can be summarized in our mission statement: “Connecting people and places in North Carolina safely and efficiently with accountability and environmental sensitivity.” Indeed, our transportation roadway network is vital for the economic and social successes of our great State.
Through our roadway network, goods are brought to market, tourists travel to our many historic and recreational attractions, and residents access their medical care, schools, and churches. Therefore, it is not an exaggeration that the economic vitality and growth of North Carolina and its communities are dependent upon our roadway network. The Department of Transportation continuously strives to safely and efficiently maintain mobility, promote effective construction and expansion of our roadways and seek out new methods and practices to meet the demands of North Carolina’s traveling public.
Just to reframe everyone's perspective, 2006 data shows North Carolina maintains over 79,000 miles, or almost 169,000 lane-miles, of roadway, structures, and traffic control devices. We are ranked second only to Texas for the number of state-maintained lane-miles, but we are ranked forty-seventh for revenue per lane mile. Additionally, the US Census Bureau’s July 2007 figures show the State’s population has now exceeded 9 million. This represents an increase of 12.6 percent just since year 2000 making North Carolina the 6th fastest growing state between the years of 2000 and 2007. For comparison, the national growth rate remains close to 7.2 percent. The momentum of this rapid growth has made North Carolina the nation's 10th most populous state.
The challenges facing the Department of Transportation in an inflation driven economy becomes very clear when faced with these real-world reminders of our expanding responsibilities toward maintaining our State’s investment in its infrastructure and providing services for a booming population. It is with due diligence the Department endeavors to meet these challenges through the continued exploration and application of new methods and practices available to the transportation industry across the country and abroad. The Superstreet is one such application.

## Slide 3: The Superstreet
A type of intersection in which minor cross-street traffic is prohibited from going straight through or left at a divided highway intersection.
Minor cross street traffic must turn right, but can then access a U-turn to proceed in the desired direction.
*Other configurations possible based on site specific conditions.
Notes: As stated earlier, the Superstreet concept refers to a reconfiguration of a traditional intersection. Simply put, it is a method to safely and efficiently manage high traffic volumes at intersections with multiple approaches along a divided highway. The Superstreet functions by redirecting through and left turning traffic on the side street approach to turn right, proceed to the nearby U-turn and then return to its original course. At first, this may seem to be a complex solution to a very simple objective – to cross the intersection or to make a left turn. However, I think you will see as we proceed that what seems complex, when designed correctly, is actually a simple and safe solution to the problems caused by congestion.

## Slide 4
Notes: Here, we see the basic lane configurations and intersection geometrics for both the conventional intersection and a superstreet intersection along a typical divided highway. There are two basic physical differences in terms of asphalt and concrete between the two types of intersections. The first, and most obvious, are the additional U-turns positioned to the left and to the right of the primary intersection. The distance between the primary intersection and the U-turn is generally specified to be within 600 to 1000 feet. The second is the addition of raised islands in the median areas. These are used to channelize traffic flow safely through the lane configurations.
The first example shown on the screen depicts a familiar left turn movement approaching the intersection from the side street in an attempt to turn left. Below, in the Superstreet configuration, left turning traffic is redirected to the right where motorists maneuver into the designated U-turn lane and navigate the U-turn in order to continue along the divided highway in the preferred direction.

## Slide 5
Notes: Likewise, in the superstreet configuration, traffic attempting to travel through the intersection and continue along the side street is also redirected to the right where motorists then merge into the designated U-turn lane, navigate the U-turn and turn right onto the side street. Therefore, full accessibility is maintained for all traffic movements at the superstreet intersection.

## Slide 6
Why Superstreets?
Notes: Now that we have established a good understanding of how the new tool in the toolbox works, let’s explore why it works. The best place to begin that process is with the question:
Why do we use superstreets?

## Slide 7
Answer:
Improved Safety
Less Travel Time
Economically Beneficial
Environmentally Responsible
Notes: Why do we use superstreets?
To:
Improved Safety;
Less Travel Time;
Economically Beneficial; and
Environmentally Responsible
All four of these objectives project personal meanings for both the public and the Department of Transportation. For motorists, they mean arriving safely and on time to offices, schools and homes while enhancing the communities where we live. For our Department, it means effectively optimizing the capacity of our existing resources to safely and efficiently connect the traveling public with the places they need to go. It means making sure we have explored every alternative to insure financial accountability as well as environmental sensitivity. It means keeping our promise to the public and it means delivering our core values to the street.

## Slide 8: Why Superstreets?
Improved Safety
Reduced likelihood of crashes, especially severe crashes such as side-collisions
Fewer threats to crossing pedestrians
Notes: At the North Carolina Department of Transportation, safety is our number one priority. The implementation of the superstreet concept by the Department reflects our dedication and continued efforts to protect public safety. superstreets reduce the risk of crashes and specifically the risk of severe crashes such as side-collisions or T-bone type accidents. Since the superstreet concept eliminates the two movements that are statistically considered a higher risk for serious injury – side street throughs and lefts -- the likelihood of severe and fatal incidents at the superstreet intersection are therefore reduced.
For the same reasons, pedestrians also benefit from the safety features of superstreets. Due to the simplification of traffic flow and the reduction of potential conflicts with turning vehicles, pedestrian safety is considerably improved.

## Slide 9
Conventional Intersection Conflict Points
Improved Safety
Notes: This illustration shows all the potential points where vehicles moving in conflicting directions may intersect, or crash. These “conflict points” are represented by the green, red and white circles that also indicate crash type. As you can see, there is a web of potential conflict points for the conventional intersection -- 32 to be exact. Collisions between vehicles traveling perpendicular to one another statistically result in the most severe injuries as drivers and/or passengers receive the brunt of impact from the side where they are the least protected. The superstreet effectively reduces severe crash types by eliminating left turning traffic from the side streets.

## Slide 10
Superstreet Conflict Points
Improved Safety
Total Conflict Points = 14
Notes: Here we have the same illustration for the superstreet with all the potential conflict points identified. As you can see, there is a dramatic reduction in the number of conflict points -- almost 50 percent. This translates to a significant reduction in risk to motorists. Looking at the diagram, conflict points resulting from perpendicular traffic movements are either eliminated or disbursed to avoid the high-risk, T-bone crashes.

## Slide 11
Improved Safety
Total Intersection Conflict Points
Conventional Intersection – 32 16 Crossing Conflicts
Superstreet Intersection – 14 2 Crossing Conflicts
Notes: The safety aspect of the superstreet is one that warrants reiteration and emphasis. To summarize, a conventional intersection has 32 conflict points versus a superstreet’s 14. Since there are fewer conflict points, there are fewer opportunities for collision. Likewise, since the high risk movements have been redirected, the superstreet also lowers the risk of severe injuries and fatal crashes, most notably side-impact type collisions.

## Slide 12: Superstreet Benefits and Capacities (Research Project 2009-06)
Notes: As more superstreets were being proposed, we wanted to know exactly how they were operating. We commissioned a research project, which a team from NC State, led by Dr. Joe Hummer, completed recently. This research project reviewed operational and safety effects from the installation of superstreets, both unsignalized, which is typical in rural areas, and signalized, which is more typical in urban or suburban settings. Rural and urban roads typically have different operating characteristics, and superstreets were no different in this regard.
12

## Slide 13: Reduction in Crashes
Safety impact by collision type for unsignalized superstreets, %
Collision Type | Crash Reduction %
Total | -46
Fatal and injury | -63
Angle and right turns | -75
Rear ends | -1
Sideswipes | -13
Left turns | -59
Other | -15
Notes: The safety data for unsignalized superstreets is significant. Total crashes were reduced about 46%, fatal and injuries about 63%, and critical angle crashes by about 75%. (This table is copied directly from their final report. The yellow indicates findings that were statistically significant.)

## Slide 14: Safety Conclusions
Unsignalized superstreets:
  Reduced collisions for total, angle and right turn, left turn, and fatal and injury
  Total collisions reduced by 46% (C-G method)

## Slide 15
Are U-turns safe?
Notes: Another concern that is often raised when talking about superstreets is that many people believe that U-turns are an unsafe movement.

## Slide 16
Accidents related to U-turn and left-turn maneuvers at unsignalized median openings occur very infrequently…
The 12 median openings in rural arterial corridors evaluated in detail in this research experienced an average of 0.20 accidents per median opening per year…
Based on these limited accident frequencies, there is no indication that U-turns at unsignalized median openings constitute a major safety concern.
Notes: The reality is that U-turns are not a major safety concern.
The perception that U-turns are dangerous may come from some downtown areas, which have signs banning U-turns. In those areas, the roadway is tight, and a U-turn maneuver may cause problems with traffic flow, especially if a vehicle’s turning radius doesn’t allow the movement to be made without backing up in the middle of the turn.
However, national and local studies, including this one, have shown that U-turns are no more dangerous than normal turns from median divided roadways. Superstreets are designed to accommodate U-turns at appropriate locations.

## Slide 17: Why Superstreets?
Reduced “wait time” or delay
Increased roadway capacity
Less Travel Time
Less Travel Time
Notes: To say superstreets reduce travel time may seem a strange idea after seeing that vehicles attempting to turn left or go straight though an intersection from a side street are actually redirected to a U-turn roughly 600 to 1000 feet away and are then channeled back toward the intersection to complete their movement. However, everyone can appreciate the value of spending less time waiting at a traffic signal for the red light to turn green.
For practical purposes, let’s use the term “wait time” as time you are delayed, or "delay" time. It would make sense then to say that the more “delaytime,” you have at an intersection; the more time it takes to travel to your destination. So, more delay yields longer travel time. The superstreet concept was designed to decrease the time vehicles are stopped at the intersection thereby decreasing travel time. If the time a vehicle remains stopped is reduced, then traffic "flow," or progression, is also improved. A positive effect begins to domino along the roadway corridor because better flow translates into the ability to manage more vehicles with the existing roadway. In effect, it optimizes the use of an existing roadway system and reduces both delay and travel time through intersections.

## Slide 18
Less Travel Time
Notes: To explain how superstreets accomplish this feat, we need to examine how traffic is controlled at signalized intersections. The simplest intersection would be one controlled by signage and traffic flows with minimal to no delay. When the number of vehicles increases beyond the volume in which motorists can safely maneuver the intersection or delays exceed what is reasonable; the intersection graduates to signalized control and a traffic signal is installed. The traffic signal assigns which lanes are allowed to advance through the intersection based on traffic volumes and the number of lanes from each approach of the intersection.
If we define all of the traffic movements {lefts, throughs and rights} that are assigned "green time" simultaneously as one "phase," then a traffic signal can be categorized based on the number of phases it operates. Referring to the slide, there are three examples shown of traffic signal operation. The first image depicts a two phase signal where “green time” alternates between the main street and the side street. From the arrows in the diagram, you can see the lefts, throughs and rights in both directions, one street at a time, are permitted to advance through the intersection. The second image is very similar. As above, lefts, throughs and rights from both directions, one street at a time, are again permitted to advance through the intersection, but a third phase is also added to ensure that the left turning vehicles from a designated approach are allowed some amount of green time with no opposing traffic. This is considered a three phase signal. The third and final image is an example of signal operation at a typical urban intersection with multilane approaches and traffic volumes that require the left, through and right movements of each approach to be separated into different phases in order to maintain safety and traffic flow. This is an example of an eight phase signal.

## Slide 19
Main Street Green Time
Less Travel Time
Notes: Now, the reason terms like delay, flow, green time and phase are relevant to today's presentation is because the superstreet concept is based upon the relationship between the number of phases an intersection manages and the amount of available green time that allows traffic to flow. Once a vehicle receives a red indication and is stopped at the intersection, delay for the motorist begins. As traffic engineers, if we can achieve longer green times and reduce the delay, we can optimize the operation of our intersections and roadways. Looking at the chart, you can see that the fewer phases controlling the intersection, the more green time is available for the progression of traffic.
For example, if a motorist is stopped at a two phase signal, then the wait time is fairly short because only one other phase has to cycle through the intersection before the right-of-way returns to the waiting motorist. The available green time that the intersection receives is divided only between the two phases. So, green time remains greater than the time the motorist is stopped and waiting.
The same philosophy holds for a three phase signal. Even though there is an additional phase to protect left turning vehicles, the wait time is still reasonable with only two other phases cycling through the intersection. Green time is reduced slightly and the time the motorist spends waiting is about equal to the time the motorist is given to progress through the intersection. Therefore, two and three phase signals are very effective for maintaining traffic flow and reducing travel time.
However, when traffic volumes increase and the number of lanes required to safely move traffic through the intersection exceeds the capacity of two and three phase signals, more phases must be added. Specifically, left turn movements must be isolated and protected from on-coming traffic. Hence, the more phases that are added, the more time the motorist spends waiting for the additional phases to cycle through. When operation of an eight phase signal is warranted, delay for the motorist is much longer, available green time is significantly less and driver frustration begins to increase. Engineers reach for tools like superstreets when even eight phase traffic signals cannot effectively manage driver demands on the roadway system.

## Slide 20
Superstreet Phasing
Less Travel Time
Notes: This diagram shows the phasing sequence of the superstreet. The superstreet essentially takes the operation of an intersection that has moved beyond the functional capacity of eight phase operation and divides the eight phases into four separate intersections each operating as a two phase signal. In effect, this restores the longer green times, re-establishes progressive traffic flow and once again reduces delay at the intersection.
Breaking down the signal phases this way, also allows engineers to work with the traffic flow in each direction of the main street separately. This makes timing traffic progression from intersection to intersection much less complicated and optimal conditions much easier to program. For motorists, this translates to fewer stops.

## Slide 21: Why Superstreets?
Economically Beneficial
Preserves the existing facility
Less expensive than an interchange
Provides good access to both sides of the main road for development
Notes: Alternatives -- this is a word we hear everyday in engineering as it applies to projects, designs and budgets. It has many different applications, but inevitably it means creating the opportunity for choice. The Department of Transportation diligently seeks to serve the public and protect the interests of our State by exploring, analyzing and providing alternatives. We explore alternative solutions like the superstreet to ensure we are delivering the most cost effective answers to the challenges facing our State's transportation infrastructure; we analyze alternative designs for each project to ensure economic accountability of the public's investment in their roadways; and we are providing alternatives that reflect the future instead of the past and emphasize our choice to lead the State in revitalizing our roadway network.
From an economic view point, the superstreet provides the State with an effective tool for reducing construction costs. In the past, when a conventional intersection had become ineffective and operated at unacceptable levels of delay, it was common practice to consider an interchange to relieve congestion. Fortunately, we now have a choice which preserves the existing roadway, delays or potentially eliminates the need for an interchange and provides balanced access to both sides of the roadway.

## Slide 22: UPS Expects To Save $600 Million by Favoring Right Hand Turns
Notes: In light of recent events, the impacts of rising fuel costs have far reaching impacts on the citizens and business that support our North Carolina communities. For companies who are dependent on the delivery of goods and services, profitability is closely linked to fuel conservation. Articles outlining corporate America’s recognition of the fiscal impacts of congestion have been prevalent in the news for several years. However, UPS has even recognized the correlation between fuel consumption and the delay of left turn phasing. The following excerpt was taken from one such article and emphasizes how superstreets can be used to support North Carolina’s business community:
Companies like UPS have taken a hit in the last couple of years as a result of rising fuel costs. Now the brown trucks of UPS are going to be getting their routes optimized to help save money. UPS delivers over 14.5 million packages a day and the trucks tend to have routes that are rarely the same. The company will be using package flow technologies to optimize the loading of packages so drivers can get them out in order, more quickly, reducing the idle time. They will also set up the daily routes, to favor right hand turns where possible, again to reduce running time. The less time trucks spend sitting in left turn lanes, the less fuel they burn. UPS is projecting savings of $600 million a year from the changes.

## Slide 23
Economically Beneficial
Notes: Conversion from a divided highway facility to a superstreet configuration requires only minimal roadway construction and right-of-way procurement. The "footprint" of a typical superstreet intersection can be contained within an area of ten acres. The total expense to the public averages close to 1.5 million dollars with design and deployment complete within 12 months.

## Slide 24
Economically Beneficial
Notes: However, this is not the case for a conventional interchange which requires significant construction. The "footprint" for a typical interchange can impact as much as 90 acres with total expense to the public reaching more than 7 million dollars to construct. Introducing bridge construction significantly lengthens the construction schedule and delivery can take from 18 months to 2 years.

## Slide 25: Environmentally Responsible
Less time spent idling at a red light
Why Superstreets?
Reduction in environmental pollutants
(exhaust fumes / fuel usage)
Less acreage impacted by construction
and permanent facility
Notes: As North Carolina’s population continues to grow and development increases along our highway system, the focus on environmental responsibility takes center stage as a vital design element in every aspect of today’s transportation industry -- in planning, design, construction and operation.
The superstreet concept is an excellent example of environmentally sensitive design sometimes referred to as building “green.” Common goals for design using this philosophy apply across every discipline of engineering and include protection of natural resources and environment, optimizing existing facilities, recycling resources, spreading environmental impacts over long-range projects, creating communities versus sprawl and encouraging mix-use development and multi-modal transportation access.
You may already recognize some of the attributes of Green Design as they applied to previous superstreet objectives. The operation of superstreets plays an important role in reducing environmental impacts in several ways. We saw how superstreets reduced the amount of time vehicles remain stopped and how this improves progression through the entire corridors. This results in less time vehicles spend idling. Therefore, fewer pollutants from exhaust are released into the atmosphere, air quality is improved and fuel consumption is also conserved. These savings have far reaching impacts for our State, our citizens and for our business communities. For companies like UPS who are dependent on delivery of goods and services, profitability is closely linked to fuel conservation and efficient routing.
We also saw a significant difference in the physical footprint of superstreets as compared to interchange alternatives. Ten acres of land use impacts versus ninety acres of drainage design, bulldozing, service roads and access control create a vivid depiction of environmental advantages.
Additionally, superstreets can delay or potentially eliminate the need for interchange construction while optimizing the capacity of the existing roadway. Access to local business and community interests are facilitated equally on both sides of the superstreet creating safer entrances and exits onto and from development sites. Both pedestrians and multi-modal transportation users are safely and efficiently accommodated. Ultimately, these designs can facilitate the development of communities and mix-use centers where retail, commercial and resident amenities are easily merged.

## Slide 26
Can Superstreets Accommodate
Semi-Trailer Combinations?
Notes: One question that usually arises over the introduction of the superstreet is the concern for Semi-trailer combinations – specifically at the U-turn intersections.
Can superstreets accommodate Semi-trailers?

## Slide 27
ABSOLUTELY!
Notes: Absolutely!
As you can see from the image, U-turns are designed with additional asphalt to allow semi-trailer combinations ample room to complete the U-turn.

## Slide 28
Notes: And, again, here you can see the semi-trailer has no trouble maneuvering the U-turn.

## Slide 29
Unsignalized
Notes: The superstreet concept is very versatile and its use does not always include heavy traffic volumes. Notice, this intersection is not signalized and is set in a fairly rural area where safety was the predominant concern. Redirecting through and left turning traffic significantly reduced the number of severe accidents at the intersection and required minimal financial outlay for construction.

## Slide 30
Signalized
Notes: This is an example of a signalized superstreet. Although traffic does not appear heavy in the photograph, please note this picture was taken one week before Christmas, in a commercial district where traffic volumes along the corridor are generated from multiple residential developments with over 1000 homes per development, large commercial retailers, and other multi-use development support such as, a medical center, office space and numerous retail centers with restaurants, fast foods, designer shops, and drug stores. The implementation of the superstreet has maintained the steady progression of traffic through the corridor and there is no evidence shown of queuing either entering or exiting the shopping center shown above.

## Slide 31
Superstreets in North Carolina
Selected Existing Locations
  US 15/501 in Chapel Hill, Orange County (Signalized)
  US 17 in Pender & New Hanover Counties (Signalized)
  US 17 in Leland, Brunswick County (Signalized)
  US 23-74 in Haywood County
  US 1 in Moore County, Vass Bypass
  NC 87 in Elizabethtown, Bladen County
  US 601 in Union County
  US 17 By-Pass in Martin and Beaufort Counties
Proposed Locations
  NC 87 in Harnett County
  Poplar Tent Road, Concord (Cabarrus County)
  NC 24-27 in Mecklenburg County
  Over 60 TIP Projects throughout the state
Notes: These are the first applications of the superstreet in the State.
They represent projects where traffic and safety factors warranted superstreet application or where superstreet design is currently under consideration.
More applications are planned across the state.

## Slide 32
2009 – Looking south above Evans Road, PM peak
US 281 (San Antonio TX)
Notes: After our success with superstreets, other states have implemented similar designs. (Some states call this concept J-Turns.)
A consultant working for the Texas turnpike authority, Pape-Dawson, contacted us for information on superstreets. They were working on the US 281 corridor north of downtown San Antonio.
This section of road was supposed to be converted to a freeway, however funding issues interrupted their plans. Handling about 75,000 vehicles a day, this corridor was a persistent bottleneck every day, as illustrated in the “before” picture in this slide.
The engineers for Pape-Dawson had done some research on possible improvements, and came across NCDOT’s work on superstreets. We assisted them in preparing information for public meetings, as well as doing brief reviews of their design plans. After implementation, this corridor is moving much quicker, saving motorists somewhere around ten-fifteen minutes a day.

## Slide 33
Notes: Here’s the signal phasing and timing information for a typical intersection on US 281. Before, the primary movement, the US 281 through moves, was getting less than half of a 3 minute signal cycle, meaning that traffic would sit idling for about 90 seconds at a time. After implementation of the superstreet, the US 281 traffic gets about 70% of a 100 second cycle, meaning that the traffic would only be stopped for a maximum of 30 seconds at a time. Since coordination of the signals is easier with the superstreet, that’s essentially the only time any motorist would be stopped along the entire corridor.

## Slide 34
As traffic congestion on U.S. Highway 281 eases due to the completion of the superstreet project, construction of new commercial and retail developments along the far North Central San Antonio corridor is ramping up.
“We are close to 90 percent leased with no pad sites left,” Elliott remarked. “We've had quite a bit of interest because of the market, which is in a high growth area. And a lot of our tenants say they feel like business has increased since the superstreet was finished.”
US 281 Superstreet Comments
San Antonio Express-News March 17, 2011
Notes: As traffic congestion on U.S. Highway 281 eases due to the completion of the superstreet project, construction of new commercial and retail developments along the far North Central San Antonio corridor is ramping up.
“We are close to 90 percent leased with no pad sites left,” Elliott remarked. “We've had quite a bit of interest because of the market, which is in a high growth area. And a lot of our tenants say they feel like business has increased since the superstreet was finished.”
Many credit the gridlock relief to the creation of a “superstreet”: a series of synchronized traffic lights and turnarounds on U.S. 281 north of Loop 1604. It's the first use of the concept in Texas.
“You still have a lot of cars out here, but they're moving,” said Irwin, Alamo Regional Mobility Authority engineering and operations director.
And, after the superstreet was completed, a columnist for the local paper wrote the following:
Superstreet, I'm sorry I doubted you
Joy! The wonks have won my heart with a time-saving traffic plan that works!
When people around here first began talking about you, I rolled my eyes. What, don't they see the endless sea of rush-hour traffic north of Loop 1604 where it meets U.S. 281? A few U-turn lanes are going to help? Ah yes — only a superstreet can save us now, I scoffed.
And then it started to happen. Friends and neighbors compared notes; traffic that used to take an hour and a half out of their days took 30 to 45 minutes, maybe. Commutes got shorter. Afternoon outings became quick trips. I couldn't believe how quickly one could motor up from the Northwoods Shopping Center to the Target on Stone Oak during the height of the silly shopping season.
I know it was you, superstreet. Now I know you and applaud you. And I don't understand why we didn't have you sooner.
Don't get me wrong — I'm not naïve enough to believe that you're the answer to all the trafficky problems that loom in the future of the growth area. Sprawl will continue, and so will congestion. I know there's only so much that you and your turning lanes can do. You're not a freeway or — GASP! — a toll road.
But I think the lesson I've learned from all of this — and I hope I'm not alone — is to keep an open mind.

## Slide 35
Superstreets
A tool for protecting North Carolina’s Strategic Highway Corridors
Notes: The Department of Transportation is committed to providing a safe, efficient and effective transportation system for the State because the economic well being of the people we serve depends upon our success. New demands are being placed on our highway system everyday as our population continues to grow and new industries require affordable access to global markets.
Meeting the transportation needs of our State requires identifying and investing in those roadways and corridors that are critical to sustaining our economic lifelines. Thus, North Carolina established its Strategic Highway Corridors.
Superstreets are one tool that the Department of Transportation can use to protect these corridors through the enhancement of safety and efficiency in an economically beneficial and environmentally responsible way.

## Slide 36: Strategic Highway Corridors
Establishes a “vision” for 5,400 miles of highway along 55 corridors throughout the state.
Primary purpose: “to provide a network of high-speed, safe, reliable highways throughout North Carolina.”
For more information visit www.ncdot.org/~shc
Notes: Of our States 79,000 miles of roadway system, approximately 7 percent of those miles were identified as being so critical to our State’s transportation system that protection was warranted. There are over 5,400 miles of highway along 55 corridors identified throughout the State. These corridors carry the majority of our State’s heavy truck and tourist traffic.
The superstreet is one tool at our disposal to help regain and maintain mobility along our State’s Strategic Highway Corridors. However, its application is not limited to the highway environment. It is proving just as effective along critical arterials struggling to accommodate the influx of population growth our State is currently experiencing.

## Slide 37: Strategic Highway Corridors
Notes: This graphic represents the major transportation routes connecting North Carolina with our neighboring states to the north, south and west. The State’s diverse natural resources, scenic interests and commercial centers are unilaterally dispersed and distributed alongside of our Strategic Corridors.

## Slide 38: Summary of Superstreet Benefits
Safety
Time savings
Increased capacity
Improved traffic flow
Access management
Land use and corridor protection
Alternative to interchange (Less $$$)
Smaller “footprint” than an interchange
Notes: We have covered a broad spectrum of information pertaining to the new tool in the Department of Transportation’s tool box. Hopefully, we have also added some interesting facts about the State and what’s new on its transportation system.
I feel confident in closing that when you approach your next superstreet, you will maneuver its traffic pattern knowing that the Department of Transportation is striving to make the routes you drive safer and more efficient; your work cost effective and accessible; and the communities and natural resources you build for your families protected and sustainable.

## Slide 39: Thank You!
Notes: I want to thank you today for coming and for sharing your time with the Department of Transportation. We understand how valuable your time is and appreciate the opportunity share with you our efforts to make traveling in this State a safe and timely journey.
For those of you have time following the presentation, there is an animated simulation of a superstreet operation. I invite you to stay for just a few minutes to observe how the superstreet mitigates congestion and provides a safe, efficient and environmentally friendly alternative to traffic control.