## Slide 1: Roundabouts in North Carolina
North Carolina Department of Transportation

## Slide 2
3 Types of Circular Intersections
  Traffic Circle
Circular Intersections
Columbus Circle – New York City
Market Square - Fayetteville
Notes: 2
There are three general types of circular intersections.
Traffic circles were first introduced in 1905 at Columbus Circle in New York City. They became popular and many were built in the first half of the 20th century, especially in the New England and Middle Atlantic states. By the 1950s and ‘60s, they fell out of favor due to poor operational characteristics. The size of the circles allowed for high speeds, and inconsistent traffic controls, especially traffic in the circle often yielded to entry vehicles, often resulted in the traffic circle “locking up” with traffic. Other geometric design issues affect safety and capacity. Many states have removed older traffic circles and replaced them with traffic signals and additional laneage for turning vehicles.

## Slide 3
3 Types of Circular Intersections
  Traffic Circle
  Traffic Calming Intersection
Circular Intersections
Notes: The second are traffic calming circles, like this one, and ones popping up in neighborhoods across the state and nation. (Durham, for instance, has a dozen or so, Raleigh even more.) The small size, and absence of splitter islands, characterize this group. Since their main purpose is traffic calming, there's a question as to whether or not they are allowed on NC State roads.

## Slide 4
3 Types of Circular Intersections
  Traffic Circle
  Traffic Calming Intersection
  Modern Roundabout
Clemmons, Forsyth Co.
NC State, Raleigh
Circular Intersections
Notes: Roundabouts are newer versions of the old traffic circles. They have certain geometric and operations characteristics that increase safety and capacity, such as:
The size is much smaller (you can usually see the entire intersection.)
Entering traffic ALWAYS yields to the circulating roadway.
Speeds are kept low (15-25MPH), both by signing and by physical (geometric) design features.
With lower speeds, traffic needs smaller gaps to enter the circle
Smoother entering (not merging) increases capacity, reduces stops, which reduces air emissions.
Roundabouts always have a physical splitter island to direct traffic around the center island.
Once in the circulating roadway (center) you have no interruptions. You do not have to yield to entering traffic, and there’s no conflict with pedestrians, bus stops, or parking maneuvers.

## Slide 5
Roundabout vs. Traffic Circle Size
Traffic Circle - ~ 800’ Diameter
Roundabout – ~ 180’ Diameter
Kingston, NY
Notes: Here you can see a comparison of size for a traffic circle in Kingston NY being converted to a multi-lane roundabout. This roundabout is about 180’ across, while the circle is close to 800’. For single lane roundabouts, a typical diameter is about 120’. The larger size of the traffic circle results in a higher travel speed within the circle. This higher speed means that entering vehicles need more time or in other words, a bigger gap, to proceed. This makes the larger traffic circle less efficient, and the smaller roundabout, even at a lower speed, can handle more traffic.

## Slide 6
Roundabout vs. Traffic Circle Deflection
Roundabout – 45-60 degree entry
Traffic Circle – 90 degree entry
Duke University
Notes: With many older traffic circles, traffic enters the roundabout “straight-on”, and must do a 90 degree turn in order to continue. Vehicles making this move must do so very slowly because of the sharp angle. With modern roundabouts, vehicles are “deflected” by splitter islands in the median, and enter the roundabout at a less severe angle, around 45-60 degrees. While the deflection before the roundabout slows vehicles to around 15-20 MPH, the angled entry allows vehicles to maintain that speed, making roundabouts more efficient than the old traffic circles.

## Slide 7
Traffic Circle - Stop
Roundabout - Yield
Roundabout vs. Traffic Circle Entry Traffic Control
Duke University
Notes: With traffic circles, because of the design, many require vehicles to stop before entry. This slows down entering vehicles even more, making the circles that more inefficient. By using Yield signs, roundabouts allow drivers to keep moving if the roundabout is clear, and they can better judge gaps, and adjust speed to enter without needing to stop.

## Slide 8
Why Roundabouts?
Safest Intersection
High Capacity / Low Delay
Good for All Modes of Traffic
Geometric Flexibility
Aesthetics
Ocean Isle, NC
Notes: So, why install roundabouts.
Here are five top reasons that we’ll discuss shortly.

## Slide 9
There are 32 conflict points at a conventional intersection.
There are only 8 conflict points at a modern roundabout
Roundabouts - Safety
Notes: How do roundabouts reduce crashes? Mainly by reducing conflict points. A conflict point is where two different vehicular paths either merge or split, or cross. There are 32 non-pedestrian conflict points at conventional intersection and only 8 at a roundabout.

## Slide 10
In the United States – 2007
    Total Crashes 48%
    Fatal/Injury Crashes in Rural Areas 78%
    Fatal/Injury Crashes in Urban Areas 60%
In North Carolina from 1999-2006
    Conversion From Stop Sign Control 41%
    Conversion From Signal Control 74%
Sources:
Insurance Institute For Highway Safety www.highwaysafety.org
NCHRP Report 572 onlinepubs.trb.org/onlinepubs/nchrp/nchrp_rpt_572.pdf
NCDOT Safety Evaluation Group www.ncdot.org/doh/preconstruct/traffic/safety/Reports/completed.html
Roundabouts - Safety
Crash Reductions Following Installation of Roundabouts
Notes: Roundabouts can help lower intersection crash rates. As this data shows, roundabouts significantly reduce crashes compared to stop-controlled and signalized intersections.

## Slide 11
Peak Hour Traffic – Usually at least as efficient (same overall delay to drivers) as traffic signals or all-way stops
Off Peak Traffic – Usually much more efficient than traffic signals.
Multi-lane roundabouts can handle as much traffic as a busy signalized intersection
Roundabouts - Capacity and Operation
Notes: For many locations, a roundabout will handle peak hour traffic as efficient, or more efficient than a traffic signal, and much more efficient than an all-way stop.
In off-peak periods with low traffic volumes on a main road, a roundabout will be more efficient, since if there’s no other traffic present, a driver entering from the side street can proceed without delay. At a signal, that driver would need to wait about ten seconds for the signal to clear (yellow and red) from the main street and then give the green signal to the side street. Roundabouts are not just for intersections with relatively low traffic. A single lane roundabout can process over 20,000 vehicles per day, while a multi-lane roundabout can handle over 40,000.

## Slide 12
Roundabouts provide a safer crossing for pedestrians
Roundabouts – Multi-Modal
Montpelier, VT
Notes: Roundabouts also provide safer and quicker crossings for pedestrians. Although in theory traffic never stops at a roundabout, the reality is that yielding by vehicles is much more frequent, making a roundabout safer than even a traffic signal with a pedestrian walk/don’t walk indication.
At a roundabout, a pedestrian travels on the outside of the circulating roadway, and crosses each leg about a car length away from the circulating roadway. This allows for a safe location where vehicles are traveling slowly, either slowing down to enter the roundabout, or still traveling slow while exiting. By not allowing pedestrians to cross to the center island, we maintain the free flow movement of vehicles in the roundabout.
If there is a crash between a motor vehicle and a pedestrian, the severity of the collision is much less, due to the slower speed of the vehicle.
At this roundabout in Montpelier, VT, which is about 300’ from a school, there are about 600 children, 800 pedestrians, and 13,000 vehicles per day. There were only 4 reportable crashes in 10 years, and injury accidents down 69% from before the roundabout was installed. North Carolina has over a dozen roundabouts next to or near schools, with no problems.

## Slide 13
PHOTOGRAPHY SOURCE: Lee Rodegerdts
Roundabouts – Multi-Modal
Roundabouts provide safer travel for cyclists
Notes: 13
Cyclists have two options for negotiating through roundabouts. One option is to use the crosswalk, following the course of pedestrians. A second option is to ride through the roundabout along the same alignment as motor vehicles.

## Slide 14
Roundabouts – Multi-Modal
Grand Junction, CO
Notes: For corridors with bike lanes, roundabouts can be designed to accommodate both types of bicycle riders. For experienced cyclists, when a bike lane ends, they can “claim the road” and use the general roadway. The speeds of both cyclists and motor vehicles are about the same, the cyclist continues through the roundabout as a vehicle, and then after exiting the roundabout, can re-enter the bike lane. Bike lanes should not be continued through a roundabout, since that would indicate that bikes should keep to the right, and motor vehicles would “cut them off” at exits. No passing of bikes (or motor vehicles) should occur in single lane roundabouts.
For less experienced bikers, this design provides an “exit ramp” as the bike lane ends, to allow a smooth transition from the bike lane to the pedestrian walkways. Bikers who take this approach should dismount and walk their bikes through the roundabout.

## Slide 15
Buses do not have trouble negotiating the roundabout, and provide a good location for bus stops
Roundabouts – Multi-Modal
North Carolina State University
Notes: Roundabouts are designed with all vehicles in mind, and buses have no problems in negotiating a roundabout, as you can see from this roundabout on the NC State campus. If space is available for a bus pullout, a location past the roundabout is preferred. If there’s no room for a pullout, a bus stop just before entering the circulating roadway is better, so that traffic in the roundabout doesn’t get blocked by the bus.

## Slide 16
Roundabouts – Geometric Flexibility
Lewisville, NC
Notes: Roundabouts provide safe, efficient operation without needing to replace or widen bridges to add turn lanes. In many locations, two-lane bridges were built at interchanges, since there was little traffic in the area at the time. Over the years, traffic volumes have grown to the point where there is significant congestion due to left-turning vehicles blocking through vehicles from moving, however there is no room to build turn lanes without replacing the bridge structure. Since roundabouts treat left-turners and through vehicles the same, roundabouts provide a much better solution at these “retrofit” locations than signals. North Carolina has three roundabout interchanges, with more being planned.

## Slide 17
Roundabouts can be designed as ovals and oblong shapes in order to achieve better movement separation and accommodate unique intersection geometry
Works well for offset T-type and multiple legged intersections
Could be an option for median divided facilities where controlling access is an issue
Roundabouts – Geometric Flexibility
Cape Coral, FL
Notes: Roundabouts don’t actually have to be round to function well. In some areas, oval or oblong shaped roundabouts can provide more efficient and safer operation than signals or stop signs. In this example from Florida, two closely spaced intersections are combined into one roundabout, without needing to realign one of the side roads to intersect across from the other side street, preserving buildings and homes.

## Slide 18
Roundabouts – Geometric Flexibility
Brunswick, MD
Notes: In this example, an oblong shaped roundabout serves six roads. Roundabouts are ideal solutions to intersections with more than four entering legs, or other unusual geometric conditions.

## Slide 19
Landscaping
Duke University
Notes: Roundabouts provide opportunities for extensive landscaping. Because of the lower speeds, the “clear zone”, which provides drivers with space to recover from mistakes, can be reduced, allowing for structures such as this low wall at this roundabout in Durham. In fact, a vertical element such as this landscaping, or other simple structures, helps motorists see that there’s something up ahead. However, nothing should be constructed in the center island that would attract pedestrian activity, as pedestrians should keep to the outside pedestrian walkways. Any landscaping or structures should be designed to be “seen from afar.”

## Slide 20
Landscaping
Ocean Isle, NC
Notes: Landscaping can feature local plants and provide a local identity (Ocean Isle)

## Slide 21
Landscaping
Bloomington, IN
Notes: Whimsical landscaping such as this one in Bloomington, IN or…

## Slide 22
Landscaping
Houten, the Netherlands
Notes: …this “UFO landing strip” hardscape in Houten, the Netherlands can bring attention to an area, and provide relief from the normal travel visions of asphalt, concrete and traffic signals.

## Slide 23
Driver Expectation
Large Trucks
Cost and Maintenance
Emergency Vehicle Access
When a roundabout is recommended for an intersection there typically is some public resistance. Some of the complaints and questions we frequently hear/deal with:
Common Concerns
Notes: In the ten-plus years of installing roundabouts in North Carolina, we have heard many concerns and worries about roundabouts, most of which are misinformation. Which is why, of course, we developed this presentation to provide accurate information about roundabouts. These items are probably the most frequently heard from the public.

## Slide 24
Driver Expectations
Notes: With older traffic circles, the rules of the road were not always consistent, sometimes allowing the circulating traffic the right-of-way, and sometimes the entering traffic. With roundabouts, the rules are consistent, with entering traffic always yielding to traffic already in the roundabout.
An additional complaint is that motorists “don’t know how to drive at a roundabout” and are confused. A roundabout is much simpler to drive through than any other intersection, since a driver in essence only needs to look to their left when entering to select a gap in traffic to enter the roundabout, and then have a clear, uninterrupted path to their exit. Although, of course, drivers should always look out for other motorists and pedestrians.
Even if a driver does something unnecessary, such as stopping before entering (when there are no cars in the roundabout), the traffic flow recovers quickly.

## Slide 25
PHOTOGRAPHY SOURCE: Lee Rodegerdts
Large Trucks
Notes: A roundabout is designed to accommodate large vehicles that require greater turning radii as they travel through the circular portion of the roundabout. A portion of the center island, appropriately called a truck apron, is usually paved to accommodate the rear wheels of the vehicle.

## Slide 26
Average Roundabout construction costs about $400,000
Maintenance is minimal (mostly mowing any additional landscaping is done by others)
Signalized intersection costs are about $100,000
Signal maintenance costs are about $3,000-5,000 annually
Construction of turn lanes is about $75,000-$150,000
Intersection Costs
Notes: The cost of construction for a roundabout is about $400,000, not including any additional right-of-way. While this is more than a typical signal installation, which is about $100,000, maintenance costs are much lower, with no significant costs beyond typical pavement maintenance and mowing. In the long term, roundabouts are often less expensive than signals. And if turn lane construction is necessary, a roundabout often will be cheaper to build than a traditional intersection, both in retrofits or in new construction.

## Slide 27
PHOTOGRAPHY SOURCE: Brian Walsh
Emergency Vehicles
Notes: Roundabouts also accommodate emergency vehicles. Motorists at roundabouts are expected to observe the same laws and courtesies as the do on other roadway facilities. When an emergency vehicle approaches the roundabout, drivers are expected to pull over to provide sufficient room for the emergency vehicle to pass. If there is not enough room for this to occur, the driver is expected to take the steps necessary to clear the way for the emergency vehicle. This may involve proceeding through the roundabout and then pulling over to the side, or yielding priority to the entering emergency vehicle.

## Slide 28
There are over 200 roundabouts in the State, about half on the State road system
The majority of the roundabouts in the State are single lane with four approaches
Multilane roundabouts are becoming more acceptable
Downtown areas
Interchange ramps
Each of the State’s 14 Transportation Divisions has at least one roundabout in operation or under construction
North Carolina Roundabout Trends
Notes: Here’s a few trends that we see in North Carolina with roundabouts.
While most of our roundabouts are still single-lane, more multi-lane roundabouts are being proposed and designed.
Many municipalities are considering roundabouts to control traffic in their downtowns, and to enhance the area.
Roundabouts provide excellent safety and operational benefits at interchanges, and help reduce construction costs.
Roundabouts are being installed across the state.
North Carolina is among the top states in the USA for roundabouts. Others include Washington, Colorado, Wisconsin, New York, Maryland and California.

## Slide 29
North Carolina Roundabouts
Inventory as of August 2010
Notes: Here’s a map of those roundabouts. It doesn’t quite stretch yet from “Murphy to Manteo”, however it does go from Franklin to Kitty Hawk. (And we are looking at a couple of roundabouts in the Murphy area.)

## Slide 30
Clemmons, Forsyth Co.
Single Lane Roundabouts
Notes: This is a picture of NCDOT’s first modern roundabout. The roundabout is located in Clemmons, on Fraternity Church Road, off of US 158, in front of Clemmons Middle School. It was installed by Division 9 in 1999, and paid for by the school.

## Slide 31
NC State, Raleigh
Single Lane Roundabouts
Notes: Here’s a roundabout on the North Carolina State campus in Raleigh. Constructed in 2003, in addition to motor vehicles, it is used by a large number of pedestrians. Because of its location at a major research university, it is one of the most studied roundabouts in the country.

## Slide 32
Single Lane Roundabouts
Moore County Airport - NC 22
Notes: This roundabout at the Moore County Airport near Southern Pines replaced a traffic signal that had to be modified because the signal poles were located in the airport’s glide path. The lane in the lower right of the picture is a bypass lane. Traffic turning right towards the community college does not enter the roundabout and merges safely downstream. The installation of a bypass lane greatly increases capacity while not reducing the safety benefits gained from a roundabout installation.

## Slide 33
Old Salem – Main St. at Salem St.
Multi-Lane Roundabouts
Notes: This roundabout in the Old Salem area of Winston-Salem was the first multi-lane roundabout built in North Carolina.

## Slide 34
Multi Lane Roundabouts
Griffith Street and
Davidson Gateway Drive
Griffith Street and Jetton Street
Davidson, NC
Notes: Multiple roundabouts can be built on a corridor, providing safe, efficient traffic operation. These two multi-lane roundabouts in Davidson are an example of that.

## Slide 35
Multi Lane Roundabouts
Notes: On any roundabout with two or more lanes in the circular portion of the roadway, a motorist next to the central island will eventually need to exit. A properly designed roundabout designates appropriate lane use on the approach and is designed to allow vehicles to make each turning movement through the roundabout without needing to change lanes. This graphic shows one possible pavement marking arrangement that accomplishes this. Note that once each vehicle enters the roundabout, they never have to change lanes to exit.

## Slide 36
Questions?